| ITN/RPI-R-2009/110 |  |
| --- | --- |
| REACTOR | instituto tecnológico e nuclear |
| Reactor | nuclear and technological institute |

The IBA Data Format IDF

version 1.0

N. P. Barradas

Sacavém, Dezembro 2009

INSTITUTO TECNOLÓGICO E NUCLEAR

Unidade de Reactores e Segurança Nuclear (URSN)

E.N. 10, 2686-953 Sacavém

CONTENTS

1	A universal data format for Ion Beam Analysis	3

1.1	Original publication and credits	3

1.2	Introduction	3

1.3	The IBA Data Format general philosophy	5

1.4	Extensibility	8

1.5	Quantities and units	10

1.6	Definition of angles	13

2	IDF URL, documentation, and distribution	14

2.1	URL	14

2.2	Documentation	14

2.3	Examples	14

3	Description of the IDF structure	15

# A universal data format for Ion Beam Analysis

## Original publication and credits

The first original publication on the IDF is co-authored by N.P. Barradas, M. Mayer, and M. Thompson. It is published in the Proc. of the 20th International Conference of Ion Beam Analysis, Nuclear Instruments and Methods in Physics Research B (2010). This is the paper that should be cited whenever referring to the IDF.

Many comments were received from different people, in particular Miguel Reis, who contributed in defining the needs of PIXE data, and Chris Jeynes, Edit Szilágyi, and Endre Kótai.

## Introduction

Data acquisition systems and data analysis codes all implement different formats to represent and store the data, the experimental conditions, any analysis parameters, the description of the sample, and others. Data acquisition systems normally support specific (sometimes proprietary) formats, and experimentalists often convert these to their own favourite formats. Popular codes developed their own data formats to read and write all this information. This is a strong barrier against interchange of data between people from different laboratories, or that use different set-ups to measure their data, different computers to store their data, and different data analysis programs to analyse their data.

We propose and describe a new IBA data format, that aspires to support all forms of IBA data in a well defined simple format permitting easy exchange between sites and analysis programs. Its main characteristics should be: 1) It can be read and understood by inspection of the file, i.e. it is ASCII. This implies it is portable amongst all hardware platforms, and it is self-explanatory 2) It is flexible enough to cater to all IBA data needs, so a file entry can correspond to one given sample, or to a group of similar samples, or to one experimental run, or it may contain simulations only, or anything else that the user may need. 3) It is easily extendable; while the most commonly used features are already included in the new data format, new needs are easy to accommodate. For instance, most data analysis codes use similar layered sample descriptions, but the codes treat roughness or equation overlays in different non-equivalent ways; code-specific entensions to the basic data format are allowed, solving this problem.

The International Atomic Energy Agency sponsored a review of existing codes for IBA data analysis, and then an intercomparison exercise of the different codes [,]. In the first meeting of the IAEA Intercomparison of IBA Software exercise [], that took place in December 2003, it was already recognised the need for an IDF, and also that XML [] fulfilled the desired characteristics. A final decision to establish the IDF was taken when the development of a universal IBA data format became the first milestone of the European Commission-supported SPIRIT [] Integrated Infrastructure Initiative, which integrates 11 leading European ion beam facilities from six member states and two associated states.

A similar approach was taken by the NeXus International Advisory Committee, that develops NeXus, an XML-based common data format for neutron, x-ray, and muon science []. The possibility of integrating IBA-specific requirements in NeXus was considered, as NeXus is being developed since 1994 by a large group of developers and users and offers many software facilities. This was discarded because NeXus is oriented towards instruments, i.e. experimental facilities, which are notoriously different in IBA and in the neutron and x-ray scattering world; to establish an IBA extension to NeXus, each separate IBA instrument would have to be defined and submitted to the NeXus International Advisory Committee (NIAC) for revision and ratification, which is a process that typically takes years, even not considering that the NIAC holds no IBA experise.

Fig. 1. IDF file almost fully collapsed; only the "beam" data group is expanded. Not all options and possibilities are included.

## The IBA Data Format general philosophy

The extensible mark-up language (XML) was developed by the World Wide Web Consortium (W3C) to structure, store, and transport data. Although often associated with the internet, XML is by no means a specific internet language, and there are many non-internet XML applications.

Fig. 2. Part of the IDF schema that defines the element “spectrum”

In particular, XML has no pre-defined tags (keywords to carry specific information). In fact, the IDF is an XML schema, that is, a definition of all the elements (also called tags) allowed, how they are structured, which information they can contain, and how it can be extended. A given file is an IDF file if it is validated against the IDF schema. The schema contains no specific information about any experiment; it just defines the structure of the IDF files. In fact, the IDF schema is the definition of the IDF data format.

For instance, we show in Fig. 1 an IDF file, where most elements are collapsed and their content is not shown. The only elements that are fully expanded are those that define the beam (note that in a complex case, the “beam” group would include definition of foils, slits, charge state distribution, and others). We show in Fig. 2 the part of the IDF schema that defines the element “spectrum”, which normally will contain all the experimental conditions as well as the spectrum as such, and also any data processing made, such as a fitted curve together with any scattering cross sections or stopping powers used in the calculation (and will not contain information about the sample structure, reserved for the element “structure” defined elsewhere). This element “spectrum” structures the relevant information in daughter (higher-level) elements such as "beam", "geometry", "data", or “process”. Each one of these is defined elsewhere in the schema, and contains further elements in a structured well-defined way. Note that not all tags defined in the schema need to be in the IDF file.

With this example in mind, the general philosophy of IDF is:

-	The basic elements of IDF are data items and data groups. Data items are e.g. “layerthickness”, or “concentration”; these data items can be real numbers, integer, or even text (e.g. “geometrytype” can be “IBM”, “Cornell”, or “general”). Data groups are logically organised (e.g. “geometry”, “stoppingpowers”, or “structure”), and can contain other data groups as well as data items.

- The information is structured as a tree. Each data group is a node of the tree. Standard tree parsing methods can be applied. The root element is always “idf”.

- The elements appear, inside the group to which they belong, in fixed order that must be respected. These pre-defined elements support most, but not all, IBA needs. However, all elements are optional, they need not appear. The apparent complexity of the data groups does not in fact exist in normal cases and simple experiments.

- Each data group can start with the elements “users” and “notes”. The group “users” should be for information on e.g. sample owner, experimentalist, data analyst.

- Any number of non-IDF elements can be inserted in any data group, at the end. They are clearly identified with a prefix, that is unique to each specific code or user that wishes to have their own elements. For instance, all NDF specific tags will be identified with the prefix “NDF:”. This maks the IDF fully flexible and extensible.

- All elements that describe a quantity have as mandatory attribute “units” (e.g. “keV”, “nm”, “1e15at/cm2”). Units must be given!

- All elements that describe a quantity have as optional attributes “quantity” (e.g. “energy”, “thickness”, arealdensity”), “uncertainty”,  “uncertaintyA” and “uncertaintyB” for types A and B, respectively, and  “uncertaintyplus” and  “uncertaintyminus” for the upper and lower limits, respectively.

- All elements that decribe a spread have as mandatory attribute “mode”, which can be “FWHM”, “sigma”, or “variance”.

- Not all units are allowed, since it would lead to severe parsing problems by software. For each quantity, only certain units are allowed. This is described in full below.

- The IDF structures data and information with top level tag “sample”; all the information relating to one given sample is given, including structure, any spectra measured (which can be more than one, or even none if it is a pure simulation), all experimental conditions for the different measurements, all calculations and simulations. In an IDF file, there can be any number of “sample” entries.

- Information about some specific data groups can be given under a top level tag "repository". For instance, different beams can be defined, or different geometries. These can then be referenced from within a given "sample" data group. This allows for conciseness, as information on the experimental conditions does not need to be repeated for each sample measured. A full explanation is given below.

## Extensibility

As said above, any number of non-IDF elements can be inserted in any data group, at the end. They are clearly identified with a prefix, that is unique to each specific code or user that wishes to have their own elements. For instance, all NDF specific tags will be identified with the prefix “NDF:”. This maks the IDF fully flexible and extensible.

In XML, extensibility is provided by the schema, that can allow (or forbid) elements not defined in the schema to be included in the instance files. In IDF, this is allowed, but the new elements must be defined in a separate, user-defined, schema. That is, user-specific tags must be defined in a user-specific schema, which is then referred to in the instance file. For instance, to include NDF-specfic tags, the root element “idf” becomes

<idf

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http:/idf.schemas.itn.pt idfv1.xsd http://ndf.schemas.itn.pt ndfv1.xsd"

xmlns="http:/idf.schemas.itn.pt"

xmlns:idf="http:/idf.schemas.itn.pt"

xmlns:ndf=”http:/ndf.schemas.itn.pt ">

The second line (xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance") is required by XML, so that the XML expression “xsi:schemaLocation” can be used in the third line (xsi:schemaLocation=" http:/idf.schemas.itn.pt idfv1.xsd http:/ndf.schemas.itn.pt ndfv1.xsd").

In this third line, we associate to the IDF file two schemas: the standard IDF schema idfv1.xsd, and the schema for NDF, ndfv0.xsd. Note that each of these schemas comes with an associated Uniform Resource Identifier (URI, which is a string that identifies an internet resource; the most common URI is the Uniform Resource Locator (URL) which identifies an internet domain address). URIs are used because they are unique; they are a way to uniquely identify one group of elements. The URI associated to a given schema does not even need to actually exist, it just needs to be unique. However, it is common to give in the URI documentation and information related to the schema.

The fourth line (xmlns="http:/idf.schemas.itn.pt") serves to define that all tags that do not have user-specific prefixes belond to the IDF schema.

The fifth line (xmlns:idf="http:/idf.schemas.itn.pt") says basically the same as the fourth, but it explicitly defines the “idf” prefix.

The sixth line (xmlns:ndf="http:/ndf.schemas.itn.pt") specifies that the the prefix “ndf” is to be used for all tags that belong to the NDF schema.

This leads, for instance in calculation 25 of the IAEA intercomparison, that requires code-specific straggling options, to have:

Fig. 3. Part of the IDF file created by NDF for calculation 25 of the IAEA intercomparison exercise, including NDF-specific tags, identifid by the prefix NDF. (Note that the schema location is not the same as descrive above, because to produce the figure we used local files.)

## Quantities and units

Accepting all possible units for all quantities would lead to a nearly impossible task of supporting and converting different sets of units. Instead, a reducd set of units for each quantity was defined as standard in IDF. On top of these, all quantities can be given with units “other”, “arbitrary”, and “none”.  The IDF standard accepted units are (u stands for micro):

time

s

ms

us

ns

density

g/cm3

1e22at/cm3

pressure

atm

bar

mbar

Torr

mTorr

mmHg

Pa

temperature

C

K

solid angle

sr

msr

srad

msrad

angle

degree

rad

mrad

fluence

uC (electrical mico Coulomb)

puC (particle micro Coulomb)

C

pC (particle Coulomb)

uCoulomb

puCoulomb (particle micro Coulomb)

Coulomb

pCoulomb (particle Coulomb)

#particles

current

nA

nAmpere

Ampere

mass

amu

g

kg

charge

q

stopping power

eV/A

keV/A

MeV/A

eV/Angstrom

keV/Angstrom

MeV/Angstrom

eV/nm

keV/nm

MeV/nm

eV/um

keV/um

MeV/um

eV/cm

keV/cm

MeV/cm

eV/m

keV/m

MeV/m

eV/(ug/cm2)

keV/(ug/cm2)

MeV/(ug/cm2)

eV/(mg/cm2)

keV/(mg/cm2)

MeV/(mg/cm2)

eV/(1e15at/cm2)

keV/(1e15at/cm2)

MeV/(1e15at/cm2)

cross section

barn

b

mbarn

mb

cm2

rr (ratio to Rutherford)

cm2/mg

cm2/ug

cm2/(1e15at/cm2)

concentration

at%

mol%

wt%

ug/g (microgram per gram)

fraction

relative

energy

eV

keV

MeV

eV^2 (for energy spread given as variance)

keV^2 (for energy spread given as variance)

MeV^2 (for energy spread given as variance)

areal density

ug/cm2

mg/cm2

1e15at/cm2

thickness, length

A

Angstrom

nm

um

mm

cm

m

Note however that quantities that describe the sample structure, thickness of foils, can be given both as areal density and as thickness.

yield

counts

counts/(uCmg/cm2) (counts per micro Coulomb per  miligram per squared centimetre)

counts/(uC1e15at/cm2)

counts/(uCug/cm2)

efficiency

fraction

relative

energy calibration parameters

any of the basic energy units, i.e. eV, keV, MeV, alone or combined with /channel, or /channel^N where N is any integer. So, for instance

eV

keV/channel

eV/channel^2

MeV/channel^3

are all allowed

resolution parameter

any of the basic energy units, i.e. eV, keV, MeV, alone or combined with ^-N where N is any integer. So, for instance

keV

MeV^-1

eV^-2

none

are all allowed

atomic level

IUPAC notation is followed, for instance

K

L1

M3

and so on

atomic transition

IUPAC notation is followed, for instance

K-L3

L1-O3

M4,5-N2,3

L2-N6(7)

and so on.

## Definition of angles

In this picture,  is the angle of incidence,  the scattering angle, and  the exit angle. We define that  must be between 0° and 90°,  must be between  0° and 180°,  must be between 0° and 180°, with values above 90° indicating transmission through the sample.

# IDF URL, documentation, and distribution

## URL

The URL that uniquely identifies the IDF is

http://idf.schemas.itn.pt/

In this URL, the schema for the IDF can be found. It comprises two files, idfv1.xsd, and idfunitsv1.xsd.

## Documentation

Besides this document, two more word documents are included; these are documentation on the schema (one document for each file), generated automatically by the XML editor we used. The files are IDF documentation v1 XMLSpy.doc and IDF documentation v1 XMLSpy units.doc.

## Examples

At this moment, two example files are given in the IDF URL. The first includes practically all the options possible in the IDF (when alternatives exist, some of the options are commented out), so it actually does not correspond to any sample or experiment. It is useful as reference only. The file is

testsmallwb1.xml

The second  corresponds to calculation 25 of the IAEA intercomparison of IBA software, as made with NDF. The file is

IAEA25_NDF.xml

We plan to prepare more files corresponding to the other calculations and analyses of real data that were presented in the IAEA intercomparison.

# Description of the IDF structure

Sentences in green italics are comments about a given group of entries. Green cursive text describes the contents of a given tag. Here, only the mandatory attributes are shown (without value). Optional attributes are not shown.

In some cases, the user must choose one of two or more options. This is clearly marked in the following description with the code word "OPTION", and "END OF OPTION" to mark where the description of the alternatives is given.

<?xml version="1.0" encoding="UTF-8"?>

<idf

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xmlns="http:// idf.schemas.itn.pt/ "

xsi:schemaLocation="http://idf.schemas.itn.pt/ D:/NDF/Nuno/IBA_IDF/idfv1.xsd"> this is the root element of the IDF data format. It includes technical information on the schema and namespace URI used, that we ommit here for clarity. Note that in this example we used for convenience a local file, and not the schema file located in the URL.

<users> every single group of tags can start with the group “users”, where information on e.g. sample owner, experimentalist, data analyst can be given. Any number of tags “user” can be given. We will omit this group from most of this description	for the sake of conciseness.

<user> name of user, such as sample owner, experimentalist, data analyst </user>

</users>

<notes>every single group of tags can have the group “notes” just after the group “users”, where any information or comments can be given. Any number of tags “note” can be given. We will omit this group from most of this description	for the sake of conciseness

<note> any text </note>

</notes>

<attributes> these are attributes of the IDF file

<idfversion> version of IDF that this file conforms to </idfversion>

<filename> name of the IDF file </filename>

<createtime> Date file was created in XML format: 2002-05-30 or 2002-05-30T09:00:0</createtime>

<updatetimes> any number of “updatetime” tags can be given.

<updatetime> Date file was updated </updatetime>

</updatetimes>

</attributes>

<sample> The IDF allows two basic ways of structuring data and information. The first one has as top level tag “sample”; all the information relating to one given sample is given, including structure, any spectra measured (which can be more than one, or even none if it is a pure simulation), all experimental conditions for the different measurements, all calculations and simulations. In an IDF file, there can be any number of “sample” entries.

<elementsandmolecules> here, the elements and molecules present in the sample are given. If both “elements” and “molecules” are present, care should be taken to ensure that they are consistent with each other

<elements> here, one “element” tag is given per element present in the sample

<nelements> number of elements present; redudant with content of “elements” tag </nelements>

<element>

<name> element present, such as 28Si, Si (natural isotopic distribution), or natSi </name>

<density units=" "> density of the element </density>

</element>

</elements>

<molecules> here, one “molecule” tag is given per molecule present in the sample. “molecule” can also be taken to be a single element.The “molecules” group should have complete information about all the sample components, for instance Si 1 O 2, Si, Ti 1 O 2 and Ti could be the “molecule” tags defined.

<nmolecules>number of molecules present; redudant with content of “molecules” tag </nmolecules>

<molecule> one given molecule (or element) is given

<name> molecule present with element name and stoichiometry separated by a white space, e.g. Si 1 O 2; SiO2 not allowed since it would lead to confusions in molecules with specified isotopes such as Si 1 18O 2</name>

<density units=" "> density of the molecule </density>

</molecule>

</molecules>

</elementsandmolecules>

<structure>here the structure of the sample is given (normally this is a result of processing and analysing the data, so it could be in the “process” group below). The normal way of describing a sample structure is a layered description. A second way is the so-called “point by point” profile, in which for each element a table (depth, concentration) is calculated by directly converting the yield in each channel into a concentration. This second method is popular for instance in HI-ERDA

<crystalstructure> text describing the crystalline structure of the sample. This can be overridden layer by layer </crystalstructure>

<layeredstructure> this is the traditional layered structure

<nlayers> number of layers in the sample. Nt strictly necessary, since it should match the number of layer entries; if it does not, it is ignored and the number of layer entries should be taken </nlayers>

<layers> contains several “layer” tags, in order of appearance: the first layer entry is the surfacemost layer, the last is the bottommost (substrate) layer

<layer> a given layer

<layerthickness units=" "> layer thickness </layerthickness>

<layeruniformity units=" " mode=" ">uniformity of the layer thicknes</layeruniformity>

<layerdensity units=" "> layer density; this overrides what was given for elements or molecules </layerdensity>

<layerelements> the elements present in the layer are given

<layerelement> one given element present in the layer

<name> element present </name>

<concentration units="%"> concentration of the element </concentration>

</layerelement>

</layerelements>

<layermolecules> the molecules or logical elements present in the layer are given. If both “layerelements” and “layermolecules” are present, care should be taken to ensure that they are consistent with each other

<layermolecule>one given molecule present in the laye

<name> logical element (e.g. molecule or element) present </name>

<concentration units=""> concentration of the molecule </concentration>

</layermolecule>

</layermolecules>

</layer>

</layers>

<equationoverlays> where code-specific equation description of concentrations is to be included </equationoverlays>

<roughness> where code-specific description of roughness	is to be included </roughness>

</layeredstructure>

<pointbypointstructure> this is the second way of giving a sample definition. This can very wel coexist with the layered description; for instance, the layered description may have be used to produce a fit, while nevertheless a point by point yield calculation was performed

<element> point by point profile for one given element

<elementname> element present </elementname>

<pbp> this is the point by point profile as such, containing as many pbpitem as there are points in the “depth, concentration” table for this element

<xaxis>

<axisname>name of the depth axis</axisname>

<axisunit> units of the depth axis </axisunit>

</xaxis>

<xerroraxis> optional

<axisname> name of the depth error axis </axisname>

<axisunit> units of the depth error axis; must be same, %, or fraction </axisunit>

</xerroraxis>

<yaxis>

<axisname> name of the concentration axis </axisname>

<axisunit> units of the concentration axis </axisunit>

</yaxis>

<yerroraxis> optional

<axisname> name of the concentration error axis </axisname>

<axisunit units of the concentration error axis: must be  same, %, or fraction </axisunit>

</yerroraxis>

<x> list of x values </x>

<xerror> optional list of x error values </xerror>

<y> list of y values </y>

<yerror> optional list of y error values </yerror>

</pbp>

</element>

</pointbypointstructure>

</structure>

<spectra> as many spectra as desired can be given

<spectrum> here one spectrum (experimental and all calculations based on it) is given, including all experimental conditions.

<log> Log parameters such as real and live time are often useful in the calculation of effective charge, as well as of pile-up

<realtime> real time, in XML period of time format e.g. PT1H25M21S </realtime>

<livetime> live time, in XML period of time format e.g. PT1H25M21S </livetime>

<deadtime> dead time, in XML period of time format e.g. PT11S </deadtime>

<starttime> time at which the experiment started e.g. 2002-05-30T09:00:00</starttime>

<stoptime> time at which the experiment ended </stoptime>

</log>

<environment>“temperature” and “pressure” are not very useful parameters. The “environment” group is here so users who have special requirements have a place to introduce user-specific environment-related tags.

<temperature units=" "> temperature during experiment </temperature>

<pressure units=" "> pressure during experiment </pressure>

</environment>

<beam> the “beam” group includes things that respect to the beam before it hits the sample, so including any slits and foils located before the sample

<beamparticle> full isotope should be specified e.g. 4He </beamparticle>

<beamZ> atomic number of beam particle, this is redudant with beamparticle </beamZ>

<beammass units=" "> atomic mass of beam particle </beammass>

<beamenergy units=" "> initial beam energy; for RNRA, NRP, PIGE, and techniques where the beam energy is scanned, this tag should be left unused </beamenergy>

<beamenergyspread mode=" " units=" "> initial energy spread of the beam </beamenergyspread>

<beamchargestate> this is the initial beam charge state before the beam hits any foils or the sample. It can be a single value or a distribution. As many beamcsstate entries are given as charge states of the initial beam. The fraction needs not be normalised

<x> list of charges for which charge state fractions will be given </x>

<xerror> optional error in charges for which charge states will be given. </xerror>

<y> list of fractions of charge states given </y>

<yerror> optional error in fractions of charge states give </yerror>

</beamchargestate>

<beamfluence units=" "> total accumulated beam fluence (usually known as charge)</beamfluence>

<beamcurrent units=" "> average beam current during the experiment </beamcurrent>

<beamangularspread units=" " mode=" "> initial angular spread of the beam </beamangularspread>

<beamshape> this is the beam shape before any slits; if no slits are specified, this is the final beam shape, otherwise the slits must be considered

<shape>initial shape of the beam, the options are “square”, “circular”, “rectangular”, “elliptical”, “other”. If it is “other”, then l1 and l2 lose meaning. If it is circular or square, only l1 is needed, l2 is ignored</shape>

<l1 units=" "> dimension of beam (e.g. side or diameter) in the plane defined by the normal to the sample and the incident beam propagation axis, in the direction normal to the incident beam propagation. In this direction, the beam spot becomes l1/cos(angle of incidence) </l1>

<l2 units=" "> dimension of beam in the orthogonal plane, in the direction normal to the incident beam propagation </l2>

</beamshape>

<slitsbeforesample> any slits that are placed before the sample (to guide or to define the beam) are given here.

<slit> one given slit. The order is not important, the relative position of slits is given by the “slitdistancetosample” tag.

<slitshape> defines the shape of the given slit

<shape> shape of the slit as seen by the beam, the options are “square”, “circular”, “rectangular”, “elliptical”, “other”. If it is “other”, then l1 and l2 lose meaning. If it is circular or square, only l1 is needed, l2 is ignored.</shape>

<l1 units=" "> dimension of slit (e.g. side or diameter) in the plane defined by the normal to the sample and the incident beam propagation axis, in the direction normal to the incident beam propagation </l1>

<l2 units=" "> dimension of slit in the orthogonal plane, in the direction normal to the incident beam propagation </l2>

<l3 units=" "> dimension of slit in the direction of beam propagation </l3>

</slitshape>

<slitdistancetosample units=" "> distance between the slit and the sample </slitdistancetosample>

</slit>

</slitsbeforesample>

<beamfoil> if the beam crosses a foil before hitting the sample, it is given here.

<foildistancetosample units=" "> distance between the foil and the sample </foildistancetosample>

<foillayers> a layered description similar to the sample is adopted.

<layer>one given layer of the foil As many layers as wanted can be given

<layerthickness units=" "> thickness of layer </layerthickness>

<layeruniformity units=" " mode=" "> uniformity of layer thickness </layeruniformity>

<layerdensity units=" "> density of layer </layerdensity>

<layerelements>

<layerelement>

<name> element present in the layer </name>

<concentration units="%"> concentration of the given element </concentration>

</layerelement>

</layerelements>

</layer>

</foillayers>

</beamfoil>

</beam>

<geometry>The experimental geometry is defined here as it pertains to scattering; the normal parameters considered in codes are used here, plus the definition of the spot in the sample. Further details on the geometry are found in the beam and instrument entries

<geometrytype>ype of geometry. Options are: Cornell, IBM, and general. If IBM or general is specified, then a given exit angle must be specified. If Cornell is specified, then the exit angle is ignored</geometrytype>

<incidenceangle units=" "> angle of incidence from sample normal. Must be between 0º and 90º </incidenceangle>

<scatteringangle units=" "> scattering angle. Must be between 0º and 180º. </scatteringangle>

<exitangle units=" "> angle of exit from sample normal. Must be between 0º and 180º, with values above 90º indicating transmission geometry </exitangle>

<spot> defines the beam spot on the sample

<shape>shape of the beam spot on the sample, the options are “square”, “circular”, “rectangular”, “elliptical”, “other”. If it is “other”, then l1 and l2 lose meaning. If it is circular or square, only l1 is needed, l2 is ignored </shape>

<l1 units=" "> dimension of spot of beam in the sample (e.g. side or diameter) in the plane defined by the beam propagation axes (in and out)</l1>

<l2 units=" "> dimension of spot of beam in the orthogonal plane </l2>

</spot>

</geometry>

<instrument> here are the things that pertain to the instrument understood as the accelerator, beam line, experimental chamber, and the such

<ionsource> text describing the ion source </ionsource>

<accelerator> text describing the accelerator </accelerator>

<beamline> text describing the beamline</beamline>

<chamber> text describing the experimental chamber</chamber>

<sampleholder> text describing the sample holder</sampleholder>

</instrument>

<detection>here are the things that pertain to the detection as such, i.e. after the detected beam leaves the sample, including stopping foils and slits after the sample, and the detector as such

<slitsaftersample> any slits located between the sample and the detector can be given here

<slit> one given slit located between the sample and the detector. Definition as for the slits before the sample

<slitshape>

<shape> </shape>

<l1 units=" "></l1>

<l2 units=" "></l2>

<l3 units=" "></l3>

</slitshape>

<slitdistancetosample units=" "></slitdistancetosample>

</slit>

</slitsaftersample>

<stoppingfoil> Taken as any foil between the sample and the detector. In a E-deltaE detector, this could be used to describe the deltaE part

<foildistancetosample units=" "> distance between foil and sample </foildistancetosample>

<foillayers> layer definition as for the sample

<layer>

<layerthickness units=" "></layerthickness>

<layeruniformity mode=" " units=""></layeruniformity>

<layerdensity units=" "></layerdensity>

<layerelements>

<layerelement>

<name> </name>

<concentration units="></concentration>

</layerelement>

</layerelements>

</layer>

</foillayers>

</stoppingfoil>

<detector> description of the detector

<detectortype>type of detector, Options are, but this will need expanding:

SSB - Silicon surface barrier or equivalent

SDD - silicon drift detector

Si(Li)

Ge(Li)

HPGe

ToF - time of flight

EdE - telescope with a foil where a small energy loss serves as particle identifier and a final detector

Bragg - Bragg chamber

MagSpec - magnetic spectrometer

ElSpec - electrostatic spectrometer

other - anything not yet in the list</detectortype>

<solidangle units=" "> solid angle of detector </solidangle>

<detectorshape> Definition as for the slits before the sample This clearly does not cover all possible detector shapes. The detectorlayers data group is more general and should be used if a more accurate definition of the detector is required.

<shape> shape of detector as seen by the beam, the options are “square”, “circular”, “rectangular”, “elliptical”, “other”. If it is “other”, then l1 and l2 lose meaning. If it is circular or square, only l1 is needed, l2 is ignored. </shape>

<l1 units=" "> dimension of detector (e.g. side or diameter) in the plane defined by the sample normal and the beam propagation axis </l1>

<l2 units=" "> dimension of detector in the orthogonal plane </l2>

<l3 units=" "> dimension of active region of detector in the direction of beam propagation </l3>

</detectorshape>

<deadlayer> description of the detector dead layer. A single layer is introduced.r

<layerthickness units=" "> thickness of the dead layer of the (SSB) detector </layerthickness>

<layeruniformity mode=" " units=" "> uniformity of the dead layer of the (SSB) detector </layeruniformity>

<layerdensity units=""> density of the dead layer of the (SSB) detector </layerdensity>

<layerelements> as for the layer definition. As many elements can be given as desired.

<layerelement>

<name> </name>

<concentration units="></concentration>

</layerelement>

</layerelements>

</deadlayer>

<entrancewindow> description of the entrance window of the detector

<layer> one for each layer, in order of appearance; the first layer entry is the surfacemost layer, the last is the layer closest to the detector

<layerthickness units=" "></layerthickness>

<layeruniformity mode=" " units=" "></layeruniformity>

<layerdensity units=" "></layerdensity>

<layerelements>

<layerelement>

<name> </name>

<concentration units=" "></concentration>

</layerelement>

</layerelements>

</layer>

</entrancewindow>

<detectorlayers> Definition of the detector as a layered structure, for a more general description. As for the sample, with first layer being the top layer first hit by the detected beam.

<layer>

<layerthickness units=" "></layerthickness>

<layeruniformity units=" " mode=" "></layeruniformity>

<layerelements>

<layerelement>

<name> </name>

<concentration units=" "></concentration>

</layerelement>

</layerelements>

</layer>

</detectorlayers>

<tof> Definition of some parameters of Time of Flight detectors

<toflength units=" "> length of the ToF </toflength>

<toftimeresolution units=" "> time resolution </toftimeresolution>

<startfoil> Definition of the start foil, as for the sample layered description. First layer is the one first seen by the beam.

<layer>

<layerthickness units=" "></layerthickness>

<layeruniformity units=" " mode=" "></layeruniformity>

<layerelements>

<layerelement>

<name> </name>

<concentration units=" "></concentration>

</layerelement>

</layerelements>

</layer>

</startfoil>

<stoptfoil> Definition of the stop foil, as for the sample layered description. First layer is the one first seen by the beam.

<layer>

<layerthickness units=" "></layerthickness>

<layeruniformity units=" " mode=" "></layeruniformity>

<layerelements>

<layerelement>

<name> </name>

<concentration units=" "></concentration>

</layerelement>

</layerelements>

</layer>

</stoptfoil>

</tof>

<distancedetectortosample units=" "> distance between detector and sample </distancedetectortosample>

</detector>

<electronics> Definition of some parameters relating to the electronics used

<amplifier> Definition of some parameters of the amplifier used

<amplifiertype> type of the amplifier, can be analogue, DSP (digital signal processor) or other </amplifiertype>

<pulseshape>-pulse of the shape, can be Gaussian, triangular, trapezoidal or other </pulseshape>

<shapingtime units=" "> shaping time of the amplifier, needed for some pileup algorithms, for Gaussian pulseshape </shapingtime>

<risetime units=" "> rise time of the pulse, needed for trapezoidal pulses </risetime>

<flattoptime units=" ">time of the flat top part of the pulse, needed for trapezoidal pulses </flattoptime>

<pur> Whether the pile up rejection system was on, off or did not exist. Options are on, off, none</pur>

<purtime units=" "> characteristic time of the pileup rejection system </purtime>

</amplifier>

</electronics>

</detection>

<calibrations> detector efficiencies and energy calibrations could also be given in the “instrument” group. However, the calibrations depend not only on the instrument, but also on the detected particle.

<detectorefficiencies> the detector can have a given efficiency, that can depend on detected energy and on the detected particle (if more that one particle is detected). These are given here.There may be more than one detector efficiency! If there are multiple ions detected, they may have different eficiency each

<detectorefficiency> Detector efficiency for one given detected particle

<efficiencyion> particle for which the detection efficiency is given; this is only necessary if more than one ion is detected simultaneously </efficiencyion>

<efficiencymode> efficiency can be introduced as a table energy/efficiency, or for given (x-ray) lines in PIXE. Options are “energy” and “line”</efficiencymode>

OPTION 1

<efficiency> This is the first method of giving the efficiency, as a table of energy/value

<xaxis> Definition of the x axis; normally "energy"

<axisname> </axisname>

<axisunit> </axisunit>

</xaxis>

<xerroraxis> Definition of the x error axis; name must be "FWHM", "sigma" or "variance"

<axisname> FWHM, sigma or variance</axisname>

<axisunit> same, %, or fraction </axisunit>

</xerroraxis>

<yaxis> Definition of the y axis; normally "efficiency"

<axisname> </axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis> Definition of the x axis; name must be "FWHM", "sigma" or "variance"

<axisname> FWHM, sigma or variance </axisname>

<axisunit> same, %, or fraction </axisunit>

</yerroraxis>

<x>list of x (energy) values</x>

<xerror> list of x error values </xerror>

<y> list of y (efficiency) values </y>

<yerror> list of y (efficiency) error values </yerror>

</efficiency>

OPTION 2

<lineefficiency>This is the second method of giving the efficiency, as a table of line/value

<xaxis> Definition of the x axis; normally "X-ray line"

<axisname> name of the x axis, normally "xrayline" or similar </axisname>

<axisunit> unit of the x axis, normally "none" </axisunit>

</xaxis>

<yaxis> Definition of the y axis; normally "efficiency"

<axisname> name of the y axis, normally "efficiency"</axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis>

<axisname> FWHM, sigma or variance </axisname>

<axisunit>same, %, or fraction </axisunit>

</yerroraxis>

<line> list of line names, e.g. K-L3 or SiKa1 </line>

<y> list of y (efficiency) values </y>

<yerror> list of y (efficiency) error values </yerror>

</lineefficiency>

END OF OPTION

</detectorefficiency>

</detectorefficiencies>

<detectorresolutions> resolution of the detecting system; this can (and normally is) different for different detected particles

<detectorresolution> resolution for one given detected particle

<resolutionion> particle for which resolution is given; this is only necessary if more than one ion is detected simultaneously </resolutionion>

<resolutionparameters> any number of values can be given here, to be interpreted as polynomial coefficients on beam energy expressed in the same units as the beam energy, starting with a0, then a1, a2, etc

<resolutionparameter mode="FWHM" units=" "> polynomial coefficient on beam energy expressed in the same units as the beam energy, starting with a0, then a1, a2, etc. Units for first are e.g. keV, for second none, for third keV^-1, etc </resolutionparameter>

</resolutionparameters>

</detectorresolution>

</detectorresolutions>

<energycalibrations> There may be more than one energy calibration! If there are multiple ions detected, they may (and normally do) have different calibration each

<energycalibration> the energy calibration is always given as a polynomial on channel number

<calibrationion> particle for which calibration is given; this is only necessary if more than one ion is detected simultaneously </calibrationion>

<calibrationmode> calibration mode. The options are “energy”, “PH” if pulse height spectra are considered, “time” for time of flight experiments, and “other”</calibrationmode>

<calibrationparameters> the calibration is given as a polynominal approximation, on channel number; a series of “calibrationparameter” tags has the polunomial coefficients

<calibrationparameter units=" "> polynomial coefficient on channel, starting with a0, then a1, a2, etc. Units for first are e.g. keV, for second keV/channel, for third keV/channel^2, etc </calibrationparameter>

</calibrationparameters>

</energycalibration>

</energycalibrations>

</calibrations>

<reactions> Here the reactions that occurr are listed. For RBS, ERDA, and PIXE, this is not strictly necessary, because the reactions can be deduced from kinematics. For NRA and NRP this is more important, even if some codes may have built-in lists of possible reactions. This could be a good place to specify cross section data to be used. However, conceptually these are separate things. One thing is reactions that occurr and particles detected that make up the data, a different thing is how this data is analysed.

<technique> technique considered, options are:

RBS - including forward scattering and non-Rutherford elastic scattering

ERDA - no matter what the beam

NRA - for non-resonant i.e. particle-particle reactions, in which a single beam energy is used and an energy spectrum is collected

NRP - for resonant reactions, in which the result is the total yield for normally a sharp resonance, and often an excitation function is measured using a range of initial beam energies. This includes PIGE and RNRA.

PIXE - no matter what the beam

other

This is the main technique. Note however, for instance in ERDA, the forward scattered primary beam can also be detected.</technique>

<reactionlist> all reactions that are of interest are described here. However, e.g.  for RBS, ERDA, and PIXE, in the absence of nuclear reactions,  there is no need to specify the reactions.

<reaction> one given reaction

<initialtargetparticle> target particle hit by the beam. For specific reactions a given isotope (e.g. 28Si) should be used; Si or natSi mean natural isotopic distribution </initialtargetparticle>

<incidentparticle> incident beam particle; This must be the same as beamparticle </incidentparticle>

<exitparticle> particle that is detected </exitparticle>

<finaltargetparticle> final target particle. Note that in e.g. 11B(1H,4He)8Be, both the 4He and the 8Be can be detected. In this case, two different separate reaction entries need to be specified, 11B(1H,4He)8Be and 11B(1H,8Be)4He </finaltargetparticle>

<reactionQ units=" "> reaction heat</reactionQ>

</reaction>

</reactionlist>

</reactions>

<data> There are many different types of data that can be measured, and it is difficult to find a universal representation. The IDF supports most normal types of data and some exotic ones as well

<datamode>The options are:

simple: x, xerror, y and yerror values are entered as lists. Each list is within a single tag. Axis name and units are also given.

line - yield for given lines; the lines are identified by a string, not a number

complex - multimensional table, with any number of variables being a function of any number of variables: y1=f(x1,...,xn), ym=f(x1,...,xn) This can in principle accomodate any type of data, including listmode</datamode>

<channelmode> Values are left, right, middle, other, unknown. This indicates that the channel number gives the left, middle or right edge of a channel.

Example: With an offset of 0 keV and 1 keV/channel channel #1 is from 1 – 2 keV for left, from 0 – 1 keV for right, and from 0.5 – 1.5 keV for middle.

In the case of non-equidistant energy steps only left and right are allowed, because the original channel edges cannot be reconstructed if only the middle of each channel is given.</channelmode>

OPTION 1

<simpledata>This is the first way of introducing (x,y) data, as a table. First, the x and y axes must be defined with name and units. Second, tthe x and y data are introduced, one at a time, in a single entry

<xaxis>

<axisname> name of the x axis, normally "channel" or similar >

<axisunit> unit of the x axis, normally "#" or "number" or similar</axisunit>

</xaxis>

<xerroraxis> It's hard to see how the channel has an error; this is provided in the IDF for completeness, but in fact, every ADC does have an error in the determination of the channel limits

<axisname> FWHM, sigma or variance </axisname>

<axisunit>same, %, or fraction </axisunit>

</xerroraxis>

<yaxis>

<axisname> name of the y axis, normally "yield"</axisname>

<axisunit> unit of the y axis, normally "counts"</axisunit>

</yaxis>

<yerroraxis>

<axisname> FWHM, sigma or variance </axisname>

<axisunit>same, %, or fraction </axisunit>

</yerroraxis>

<x>list of values</x>

<xerror> list of values </xerror>

<y> list of values </y>

<yerror> list of values </yerror>

</simpledata>

OPTION 2

<complexdata>This is the second way of introducing data. Practically any type of data can be described with this way, from the simple to the very complex, including.multidimensional data This is verbose, but rather general

<datadimensions> Two integer values are needed, the first is n (the number of x variables) the second is m (the number of y dependent variables)

<datadimensionx> number of x variables, excluding"timestamp" and "line"</datadimensionx>

<datadimensiony> number of y variables </datadimensiony>

</datadimensions>

<xaxes> definition of the x axes, one per x variable. Note that error axes must aso be defined explicitly

<axis> One per quantity in order, so its number should match what is in datadimensionx. For listmode, timestamp should be specified since this is standard in XML

<axisname> name of an x axis </axisname>

<axisunit> units of an x axis (not restricted to IDF standard units)</axisunit>

</axis>

</xaxes>

<yaxes> definition of the y axes, one per y variable. Note that error axes must aso be defined explicitly

<axis> One per quantity in order, so its number should match what is in datadimensiony

<axisname> name of an y axis </axisname>

<axisunit> units of an y axis (not restricted to IDF standard units) </axisunit>

</axis>

</yaxes>

<dataentries>a series of dataentry entries. Aspectrum normally consists of many dataentry entries, for instance, a 512 channel RBS spectrum will have 512 dataentry entries. Each dataentry normally has several dataitem entries: one per quantity in order, so its number should match datadimensionx+datadimensiony. Note that "timestamp" and "line" are NOT included in datadimensionx

<dataentry>

<timestamp> time stamp used in list mode, in XML format e.g. 2003-05-30T09:00:00 </timestamp>

<line> (x-ray or -ray) line for each a yield is given </line>

<dataitem> numeric data item, the number of dataitem in a dataentry should match datadimensionx+datadimensiony. </dataitem>

</dataentry>

</dataentries>

</complexdata>

OPTION 3

<linedata>This is the third way to introduce data, specific for PIXE. A list of (e.g. xray) lines is given, then a list of the corresponding yields; this can be used e.g. as output of a PIXE code, that takes the spectrum and produces a list of line/yield. Or it can be used to output e.g. a list of the energies corresponding to given lines

<lineaxis>

<axisname> name of the x axis, normally "xrayline" or similar </axisname>

<axisunit> unit of the x axis, normally "none"</axisunit>

</lineaxis>

<yaxis>

<axisname> name of the y axis, normally "yield"</axisname>

<axisunit> unit of the y axis, normally "counts"</axisunit>

</yaxis>

<yerroraxis>

<axisname> FWHM, sigma or variance </axisname>

<axisunit>same, %, or fraction </axisunit>

</yerroraxis>

<line> list of line names, e.g. K-L3 or SiKa1, separated by white spaces. Each white space is taken to separate two line names</line>

<y> list of values </y>

<yerror> list of values </yerror>

</linedata>

OPTION 4

<datafile> This is the fourth way of introducing data, by inputing a given external data file. The filesource can be a given code, or a given lab. The fileformat should be a codeword understood by who created it (e.g. "rbs" for an rbs RUMP file)

<filename>name of the file</filename>

<fileformat> format  of the file </fileformat>

<filesource> source of the file </filesource>

</datafile>

END OF OPTION

</data>

<process> here come the things that relate to the data analysis, including cross sections and stopping powers used, straggling models, simulations made, and anything else

<physicsdefaults> the physicsdefaults data group defines defaults to be used for cross sections, stopping powers, energy spread, etc. They can be overriden for any given simulation

<crosssectiondefault> This defines the dafaults on how to handle cross sections. The defaults can be overridden by inputing given cross sections for given reactions

<Rutherford> logical (true or false), whether Rutherford cross sections are the default or not. “true” only makes sense for RBS and ERDA </Rutherford>

<screening> defines default for screening. Andersen, Ecuyer, or none </screening>

<computercode> if a computer code was used to calculate or produce the cross section, its details should be given here

<name> name of the code used </name>

<version> version of the code used </version>

<builddate> build date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</builddate>

<releasedate> release date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</releasedate>

</computercode>

</crosssectiondefault>

<stoppingpowerdefault> This defines the defaults on how to handle stopping powers. The defaults can be overridden by inputing given stopping powers for given systems. The main defaults should match the usual codes.

<computercode> if a computer code was used to calculate or produce the stopping power, its details should be given here

<name> name of the code used </name>

<version> version of the code used </version>

<builddate> build date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</builddate>

<releasedate> release date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</releasedate>

</computercode>

</stoppingpowerdefault>

<energyspreaddefault> This data  group is mainly a series of flags that inform where some effect that affect the energy spread of the beam are included in any calculation. Actual calculation requires a series of values taken from different places in the file. The default given here can be overridden for any given ion/target particle combination.

<energylossstraggling> Basic model to calculate energy loss straggling, e.g. Bohr, Chu, none </energylossstraggling>

<multiplescattering> logical flag, true/false if the effect of multiple scattering on energy spread is to be calculated or not </multiplescattering>

<Dopplereffect> logical flag, true/false if the effect of the Doppler effect on energy spread is to be calculated or not </Dopplereffect>

<beamangularspread> logical flag, true/false if the effect of the beam angular spread on energy spread is to be calculated or not </beamangularspread>

<geometricspread>

<beamsize> logical flag, true/false if the effect of the finite beam size on energy spread is to be calculated or not </beamsize>

<detectoraperture> logical flag, true/false if the effect of the finite detector aperture size on energy spread is to be calculated or not </detectoraperture>

</geometricspread>

<Tschalareffect> logical flag, true/false if the Tschalar effect is to be calculated or not </Tschalareffect>

<computercode> if a computer code was used to calculate or produce the energy spread, its details should be given here

<name> name of the code used </name>

<version> version of the code used </version>

<builddate> build date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</builddate>

<releasedate> release date of the code used in XML format, elgl 2002-05-30 or 2002-05-30T09:00:00</releasedate>

</computercode>

</energyspreaddefault>

<PIXEdefault>PIXE needs a host of parameters that often come from given data bases, data collections, or computer codes. The defaults for PIXE are given in IDF as references to one of these sources, introducing name, builddate and release date. The name can be for instance a given publication, a given database, a given computer code, or anything else that the PIXe community recognises.

<ionizationcrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</ionizationcrosssections>

<Xrayproductioncrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</Xrayproductioncrosssections>

OPTION 1 either totalabsorptioncrosssection or massabsorptioncoeffficient can be used, since both names are common in PIXE

<totalabsorptioncrosssection>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</totalabsorptioncrosssection>

OPTION 2

<massabsorptioncoeffficients>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</massabsorptioncoeffficients>

END OF OPTION

<fluorescenceyields>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</fluorescenceyields>

<costerkroningyields>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</costerkroningyields>

<branchingratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</branchingratios>

<transitionratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</transitionratios>

<photoelectricionizationcrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</photoelectricionizationcrosssections>

<jumpratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</jumpratios>

</PIXEdefault>

</physicsdefaults>

<simulations> This data group contains all the simulations made

<simulation>Contains one simulation made

<physics>

<crosssections> everything that relates to cross sections of this simulation should be here, and it will override the default given

<crosssection>here cross sections can be be introduced for one given reaction, either as a file name or as (energy,cross section) tabular data. Both of these override the crosssectiondefault.

<crosssectionframe> frame of reference where cross section is given, cm (for center of mass) or lab (for laboratory)</crosssectionframe>

<crosssectiontype> type of cross section, either total or differential </crosssectiontype>

<reaction> reaction for which cross section is given. For RBS and ERDA, only the target particle needs be given.

<initialtargetparticle> target particle hit by the beam. For specific reactions a given isotope should be used, otherwise e.g. Si or natSi mean natural isotopic distribution </initialtargetparticle>

<incidentparticle> incident beam particle </incidentparticle>

<exitparticle> particle that is detected </exitparticle>

<finaltargetparticle> final target particle </finaltargetparticle>

<reactionQ units=" "> reaction heat, needed to specify different states of the exit particle </reactionQ>

</reaction>

OPTION 1

<crosssectionfile>This is the first possibile way of inputing a given cross section. Here a given file name containing a cross section can be give

<filename> name of the file </filename>

<fileformat> format of the file (e.g. “r33”, or “other”)</fileformat>

<filesource> text defining where the file comes from </filesource>

</crosssectionfile>

OPTION 2

<crosssectiondata> this is the second  possible way of inputing a given cross section. Here actual cross section data can be given in full. The x and y axes are defined in the usual way, with optional xerror and yerror axes as well

<xaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xaxis>

<xerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xerroraxis>

<yaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis>

<axisname>sigma</axisname>

<axisunit>%</axisunit>

</yerroraxis>

<x>list of numeric entries</x>

<xerror> list of numeric entries </xerror>

<y> list of numeric entries</y>

<yerror> list of numeric entries </yerror>

</crosssectiondata>

OPTION 3

<crosssectionoverride> This is the third possible  way of inputing a given cross section. Here a given model can be given with exactly the same structure as the default, overriding the default

<Rutherford> </Rutherford>

<computercode>

<name> </name>

<version></version>

<builddate></builddate>

<releasedate></releasedate>

</computercode>

</crosssectionoverride>

END OF OPTION

</crosssection>

</crosssections>

<stoppingpowers> everything that relates to stopping powers should be here

<stoppingpower> Stopping powers for one given ion/element pair will be given, either as a file name or as (energy,stopping power) tabular data. Both of these override the stoppingpowerdefault.

<ion> ion for which stopping power is given </ion>

<ionchargestate> charge state of ion for which stopping power is given, 0 (or if the tag is absent) will mean equilibrium charge state </ionchargestate>

<targetelement> target element for which stopping power is given </targetelement>

<stoppingmode> stopping power mode: electronic, nuclear, or total </stoppingmode>

OPTION 1

<stoppingpowerfile> This is the first possibile way of inputing a given stoppingpower. Here a given file name containing a stoppingpower can be given

<filename> name of the file </filename>

<fileformat> format of the file (e.g. “SRIM”, or “other”)</fileformat>

<filesource> text defining where the file comes from. This is not the same as fileformat; fileformat=SRIM specifies a given format, not a specific origin of the file </filesource>

</stoppingpowerfile>

OPTION 2

<stoppingpowerdata> This is the second  possibile way of inputing a given stopping power. Here actual stopping power data can be given in tabulated form using the usual data structure.

<xaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xaxis>

<xerroraxis>

<axisname> axisname>

<axisunit>fraction</axisunit>

</xerroraxis>

<yaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yerroraxis>

<x></x>

<xerror></xerror>

<y></y>

<yerror></yerror>

</stoppingpowerdata>

OPTION 3

<stoppingpoweroverride> This is the third possible  way of inputing a given stopping power. Here a given model can be given, overriding the default

<computercode>

<codename></codename>

<codeversion></codeversion>

<codebuilddate>0</codebuilddate>

<codereleasedate></codereleasedate>

</computercode>

</stoppingpoweroverride>

END OF OPTION

</stoppingpower>

</stoppingpowers>

<energyspreads> everything that relates to energy spread should be here

<energyspread> This group is mainly a series of flags that inform where some effect that affect the energy spread of the beam are included in any calculation. Actual calculation requires a series of values taken from different places in the file. Here one given energy spread will be given, either as a file name or as (energy,energy spread) tabular data. Both of these override the energyspreaddefault

<ion> ion for which energy spread is given </ion>

<ionchargestate> charge state of ion for which energy spread is given, 0 (or if the tag is absent) will mean equilibrium charge state </ionchargestate>

<targetelement> target element for which energy spread is given </targetelement>

< energyspreadmode > energy spread mode: electronic, nuclear, or total </ energyspreadmode >

OPTION 1

<energyspreadfile>This is the first possibile way of inputing a given energy spread. Here a given file name containing a energy spread can be given

<filename> </filename>

<fileformat> </fileformat>

<filesource> </filesource>

</energyspreadfile>

OPTION 2

<energyspreaddata>This is the second possible way of inputing a given energy sprea. Here actual energy sprea data can be given in full using the usual data structure.

<xaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xaxis>

<xerroraxis>

<axisname> axisname>

<axisunit>fraction</axisunit>

</xerroraxis>

<yaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yerroraxis>

<x></x>

<xerror></xerror>

<y></y>

<yerror></yerror>

</energyspreaddata>

OPTION 3

<energyspreadoverride>This is the third way of introducing a given energy spread, by over riding the default with a new model, with exactly the same structure as the default

<energylossstraggling> </energylossstraggling>

<multiplescattering> </multiplescattering>

<Dopplereffect> </Dopplereffect>

<beamangularspread> </beamangularspread>

<geometricspread>

<beamsize> </beamsize>

<detectoraperture> </detectoraperture>

</geometricspread>

<Tschalareffect> </Tschalareffect>

<computercode>

<codename></codename>

<codeversion></codeversion>

<codebuilddate></codebuilddate>

<codereleasedate></codereleasedate>

</computercode>

</energyspreadoverride>

END OF OPTION

</energyspread>

</energyspreads>

<PIXE>The PIXE basic data requirements can be a bit more complicated then for other techniques; IDF allows redefining the entire default for a given simulation, together with entering single data for specific parameters of specific lines and transitions. This leads to a fairly complex structure.

<PIXEoverride> whatever was in the default can be overridden here, by introducing different data bases. The data bases affect all elements.

<ionizationcrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</ionizationcrosssections>

<Xrayproductioncrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</Xrayproductioncrosssections>

OPTION 1

<totalabsorptioncrosssection>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</totalabsorptioncrosssection>

OPTION 2

<massabsorptioncoeffficients>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</massabsorptioncoeffficients>

END OF OPTION

<fluorescenceyields>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</fluorescenceyields>

<costerkroningyields>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</costerkroningyields>

<branchingratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</branchingratios>

<transitionratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</transitionratios>

<photoelectricionizationcrosssections>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</photoelectricionizationcrosssections>

<jumpratios>

<name> </name>

<builddate></builddate>

<releasedate></releasedate>

</jumpratios>

</PIXEoverride>

OPTION 1 either massabsorptioncoeffficients or totalabsorptioncrosssections are given, not both. The structure inside is exactly the same. It will be given only for totalabsorptioncrosssections

<massabsorptioncoeffficients>

structure ommitted, mirrors that of totalabsorptioncrosssections

</massabsorptioncoeffficients>

OPTION 2

<totalabsorptioncrosssections>

<totalabsorptioncrosssection> one given total absorption cross section

<element>target element for which the total absorption cross section is given</ element >

OPTION 1

<totalabsorptioncrosssectiondatabase> This is the first possible way of inputing a given totalabsorptioncrosssection Here a database can be given

<name> </name>

<version></version>

<builddate></builddate>

<releasedate></releasedate>

</totalabsorptioncrosssectiondatabase>

OPTION 2

<totalabsorptioncrosssectionfile> This is the second possible way of inputing a given totalabsorptioncrosssection Here a given file name containing a totalabsorptioncrosssection can be given

<filename> </filename>

<fileformat> </fileformat>

<filesource> </filesource>

</totalabsorptioncrosssectionfile>

OPTION 3

<totalabsorptioncrosssectiondata> This is the third	possible way of inputing a given totalabsorptioncrosssection. Here actual totalabsorptioncrosssection data can be given in full using the usual data structure

<xaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xaxis>

<xerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xerroraxis>

<yaxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yaxis>

<yerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yerroraxis>

<x>.</x>

<xerror></xerror>

<y></y>

<yerror></yerror>

</totalabsorptioncrosssectiondata>

END OF OPTION

</totalabsorptioncrosssection>

</totalabsorptioncrosssections>

END OF OPTION

Specific parameters can be introduced for given elements and atomic levels or transitions

<fluorescenceyields>

<fluorescenceyield> any number of fluorescenceyield tags can be under fluorescenceyields

<element> </element>

<level> </level>

<value units=" "></value>

</fluorescenceyield>

<fluorescenceyield>

<element> </element>

<level> </level>

<value units=" "></value>

</fluorescenceyield>

</fluorescenceyields>

<costerkroningyields>

<costerkroningyield>

<element> </element>

<level1> </level1>

<level2> </level2>

<value units=" "></value>

</costerkroningyield>

</costerkroningyields>

<branchingratios>

<branchingratio>

<element> </element>

<level1> </level1>

<level2> </level2>

<value units=" "></value>

</branchingratio>

</branchingratios>

OPTION 1

<transitionratios>

<transitionratio>

<element> </element>

<transition1> </transition1>

<transition2> </transition2>

<value units=" "></value>

</transitionratio>

</transitionratios>

OPTION 2

<linewidths>

</linewidth>

<element> </element>

<transition1> </transition1>

<transition2> </transition2>

<value units=" "></value>

<linewidth>

</linewidths>

END OF OPTION

<photoelectricionizationcrosssections>

<photoelectricionizationcrosssection>

<element> </element>

<level> </level>

<value units=" "></value>

</photoelectricionizationcrosssection>

</photoelectricionizationcrosssections>

<jumpratios>

<jumpratio>

<element> </element>

<level1> </level1>

<level2> </level2>

<value units=" "></value>

</jumpratio>

</jumpratios>

</PIXE>

</physics>

<simulationtype> Several types of simulations can be defined, depending on the “simulationtype” flag:

total: structure of the simulated data is identical to what was specified in the "dataentries" group of the "data" group. In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values

partialelement: the structure of the simulated data is similar to what was specified in the "dataentries" group of the "data" group. The x and y axes are exactly the same, but the simulation is for scattering off one single target element. This is useful to output in a simple way the calculate partial spectrum of a given element in RBS or ERDA.In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values. If the targetlayer is also specified, then the simulation is for the contribution of the given element in the specified layer only.

reaction: This is the third way to present a simulation. When simulationtype is "reaction", then one given reaction is simulated and presented. This becomes quite independent of the structure given in the "data" group, because the quantities can be all different. Suppose an RBS spectrum given in "data" as channel and total yield. Here, the simulated partial spectrum of one of the elements  is to be presented as energy and elemental yield. Also, this can be used for a pure simulation, even for a complete spectrum; if in "reaction" only the incidentparticle is given, then all reactions are considered to be included.

The calculations as such are introduced with the same options as for the data, i.e. simpledata, linedata, and complexdata</simulationtype>

OPTION The tags initialtargetparticle and targetlayer can be introduced only if simulationtype is "partialelement".

<initialtargetparticle>target particle for which the simulation is made</initialtargetparticle>

<targetlayer>if given, the simulation is only for the initial target particle in this specific layer</targetlayer>

END OF OPTION

OPTION The tags reaction, datamode, and channelmode can be introduced only if simulationtype is "reaction".

<reaction>The reaction for which data is presented has to be given. Note that to simply state the detected element for which the simulation is given is sometimes not enough: Suppose for instance coexistence of a (a,p) nuclear reaction and a-ERDA of hydrogen in the sample

<initialtargetparticle></initialtargetparticle>

<incidentparticle></incidentparticle>

<exitparticle></exitparticle>

<finaltargetparticle></finaltargetparticle>

</reaction>

<datamode> </datamode>

<channelmode> </channelmode>

END OF OPTION

OPTION 1

<simpledata> This is the first  way of introducing a simulation.

<xaxis>

<axisname></axisname>

<axisunit></axisunit>

</xaxis>

<xerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</xerroraxis>

<yaxis>

<axisname></axisname>

<axisunit></axisunit>

</yaxis>

<yerroraxis>

<axisname> </axisname>

<axisunit> </axisunit>

</yerroraxis>

<x></x>

<xerror></xerror>

<y></y>

<yerror></yerror>

</simpledata>

OPTION 2

<complexdata>This is the second way of introducing a simulation. Practically any type of data can be described with this way, from the simple to the very complex, including.multidimensional data This is verbose, but rather general

<datadimensions> Two integer values are needed, the first is n (the number of x variables) the second is m (the number of y dependent variables)

<datadimensionx> number of x variables, excluding"timestamp" and "line"</datadimensionx>

<datadimensiony> number of y variables </datadimensiony>

</datadimensions>

<xaxes> definition of the x axes, one per x variable. Note that error axes must aso be defined explicitly

<axis> One per quantity in order, so its number should match what is in datadimensionx. For listmode, timestamp should be specified since this is standard in XML

<axisname> name of an x axis </axisname>

<axisunit> units of an x axis (not restricted to IDF standard units)</axisunit>

</axis>

</xaxes>

<yaxes> definition of the y axes, one per y variable. Note that error axes must aso be defined explicitly

<axis> One per quantity in order, so its number should match what is in datadimensiony

<axisname> name of an y axis </axisname>

<axisunit> units of an y axis (not restricted to IDF standard units) </axisunit>

</axis>

</yaxes>

<dataentries>a series of dataentry entries. Aspectrum normally consists of many dataentry entries, for instance, a 512 channel RBS spectrum will have 512 dataentry entries. Each dataentry normally has several dataitem entries: one per quantity in order, so its number should match datadimensionx+datadimensiony. Note that "timestamp" and "line" are NOT included in datadimensionx

<dataentry>

<timestamp> time stamp used in list mode, in XML format e.g. 2003-05-30T09:00:00 </timestamp>

<line> (x-ray or -ray) line for each a yield is given </line>

<dataitem> numeric data item, the number of dataitem in a dataentry should match datadimensionx+datadimensiony. </dataitem>

</dataentry>

</dataentries>

</complexdata>

OPTION 3

<linedata>This is the third way to introduce a simulation, specific for PIXE. A list of (e.g. xray) lines is given, then a list of the corresponding yields; this can be used e.g. as output of a PIXE code, that takes the spectrum and produces a list of line/yield. Or it can be used to output e.g. a list of the energies corresponding to given lines

<lineaxis>

<axisname> name of the x axis, normally "xrayline" or similar </axisname>

<axisunit> unit of the x axis, normally "none"</axisunit>

</lineaxis>

<yaxis>

<axisname> name of the y axis, normally "yield"</axisname>

<axisunit> unit of the y axis, normally "counts"</axisunit>

</yaxis>

<yerroraxis>

<axisname> FWHM, sigma or variance </axisname>

<axisunit>same, %, or fraction </axisunit>

</yerroraxis>

<line> list of line names, e.g. K-L3 or SiKa1, separated by white spaces. Each white space is taken to separate two line names</line>

<y> list of values </y>

<yerror> list of values </yerror>

</linedata>

OPTION 4

<datafile> This is the fourth way of introducing a simulation, by inputing a given external data file. The filesource can be a given code, or a given lab. The fileformat should be a codeword understood by who created it (e.g. "rbs" for an rbs RUMP file)

<filename>name of the file</filename>

<fileformat> format  of the file </fileformat>

<filesource> source of the file </filesource>

</datafile>

END OF OPTION

</simulation>

</simulations>

</process>

</spectrum>

</spectra>

</sample>

<repository> The repository data group is an alternative way structuring the information and data in IDF. This is appropriate when for instance many different samples were measured with the same or similar experimental conditions (as in an experimental run). This way is more concise, as information on the experimental conditions does not need to be repeated for each sample measured. The method is to define independently e.g. all possible “beam” groups, that is, all the different beams to be considered, all possible different “elementsandmolecules”, all possible “geometry” groups, all possible “instrument” groups, all possible “detection” groupss, all possible “detectorefficiency” groupss, all possible “detectorresolution” groups, all possible “energycalibration” groups. Each group is given an unique identifie, an attribute called “id”. Then, for each sample and spectrum, reference back to the appropriate group. This is made with an attribute called “ref” that points to the “id”. In a given sample, both methods are allowed, i.e. , a full definition can be given for some data groups, while referencing a definition given in the repository can be used for other datagroups. The only restriction is that if a datagroup is defined by referencing, then it can not be partially re-defined, i.e. it can contain only the ref="" attribute, and no child elements.

<elementsandmoleculesrepository>

<elementsandmolecules id=" ">

here a full definition of the elementsandmolecules structure as given above is made. As many elementsandmolecules entries can be given, each one defining one set of values to be referenced in "sample" entries

</elementsandmolecules>

</elementsandmoleculesrepository>

<beamrepository>

<beam id=" ">

here a full definition of the beam structure as given above is made. As many beam entries can be given, each one defining one set of values to be referenced in "sample" entries

</beam>

</beamrepository>

<geometryrepository>

<geometry id=" ">

here a full definition of the geometry structure as given above is made. As many geometry entries can be given, each one defining one set of values to be referenced in "sample" entries

</geometry>

</geometryrepository>

<instrumentrepository>

<instrument id=" ">

here a full definition of the instrument structure as given above is made. As many instrument entries can be given, each one defining one set of values to be referenced in "sample" entries

</instrument>

</instrumentrepository>

<detectionrepository>

<detection id=" ">

here a full definition of the detection structure as given above is made. As many detection entries can be given, each one defining one set of values to be referenced in "sample" entries

</detection>

</detectionrepository>

<calibrationsrepository>

<detectorefficiency id=" ">

here a full definition of the detectorefficiency structure as given above is made. As many detectorefficiency entries can be given, each one defining one set of values to be referenced in "sample" entries

</detectorefficiency>

<detectorresolution id=" ">

here a full definition of the detectorresolution structure as given above is made. As many detectorresolution entries can be given, each one defining one set of values to be referenced in "sample" entries

</detectorresolution>

<energycalibration id=" ">

here a full definition of the energycalibration structure as given above is made. As many energycalibration entries can be given, each one defining one set of values to be referenced in "sample" entries

</energycalibration>

</calibrationsrepository>

</repository>

<sample>this is an example of how the repository can be used. the "ref" attribute must point to an "id" attribute with the same name, defined in the repository. Here, only the data groups structure, reactions, data, and process are actually given. Note that, if a reference is made to an id that is not defined in the repository, the file is not valid.

<elementsandmolecules ref=" "/>

<structure>full definition to be given here</structure>

<spectra>

<spectrum>

<beam ref=" "/>

<geometry ref=" "/>

<instrument ref=" "/>

<detection ref=" "/>

<calibrations>

<detectorresolutions>

<detectorresolution ref=" "/>

</detectorresolutions>

</calibrations>

<reactions> full definition to be given here </reactions>

<data> full definition to be given here </data>

<process> full definition to be given here </process>

</spectrum>

</spectra>

</sample>

</idf>

References

Appendix I: XMLSpy documentation for Schema idfv1.xsd

Schema idfv1.xsd

| schema location: | D:\NDF\Nuno\IBA_IDF\idfv1.xsd |
| --- | --- |
| attribute form default: | unqualified |
| element form default: | qualified |
| targetNamespace: | http://schemas.itn.pt/idf |

| Elements | Groups | Complex types | Simple types | Attr. groups |
| --- | --- | --- | --- | --- |
| amplifier | experimental | atomicparameter1levelType | amplifiertypeType | id |
| attributes | simulationtypepartialelement | atomicparameter2levelType | calibrationmodeType | ref |
| beam | simulationtypereaction | atomicparameter2transitionType | channelmodeType |  |
| beamrepository | simulationtypetotal | axesType | crosssectionframeType |  |
| calibrationparameters | usersnotes | axisconcentrationType | crosssectiontypeType |  |
| calibrations |  | axiscrosssectionType | datamodeType |  |
| calibrationsrepository |  | axisdepthType | detectortypeType |  |
| crosssection |  | axisefficiencyType | efficiencymodeType |  |
| crosssections |  | axisenergyspreadType | geometrytypeType |  |
| data |  | axisenergyType | pulseshapeType |  |
| datadimensions |  | axiserrorType | purType |  |
| dataentries |  | axisstoppingpowerType | screeningType |  |
| dataentry |  | axisType | shape2dtypeType |  |
| detection |  | branchingratiosType | simulationtypeType |  |
| detectionrepository |  | codedatabaseType | stoppingmodeType |  |
| detector |  | complexdataType | techniqueType |  |
| detectorefficiencies |  | complexsimulationType |  |  |
| detectorefficiency |  | costerkroningyieldsType |  |  |
| detectorresolution |  | crosssectiondefaultType |  |  |
| detectorresolutions |  | energyspreaddefaultType |  |  |
| electronics |  | fileType |  |  |
| element |  | fluorescenceyieldsType |  |  |
| elements |  | foilType |  |  |
| elementsandmolecules |  | jumpratiosType |  |  |
| elementsandmoleculesrepository |  | layerelementType |  |  |
| energycalibration |  | layersType |  |  |
| energycalibrations |  | layerType |  |  |
| energyspread |  | linedataType |  |  |
| energyspreads |  | linesimulationType |  |  |
| environment |  | linewidthsType |  |  |
| equationoverlays |  | massabsorptioncoeffficientsType |  |  |
| geometricspread |  | massabsorptioncoeffficientType |  |  |
| geometry |  | notesType |  |  |
| geometryrepository |  | pbpelementType |  |  |
| idf |  | photoelectricionizationcrosssectionsType |  |  |
| instrument |  | pixedefaultType |  |  |
| instrumentrepository |  | shape2dType |  |  |
| layeredstructure |  | shape3dType |  |  |
| layerelements |  | simpledatacrosssectionType |  |  |
| layermolecules |  | simpledatadepthconcentrationType |  |  |
| log |  | simpledataefficiencyType |  |  |
| molecule |  | simpledataenergyspreadType |  |  |
| molecules |  | simpledatastoppingpowerType |  |  |
| physics |  | simpledataType |  |  |
| physicsdefaults |  | simplesimulationType |  |  |
| PIXE |  | slitsType |  |  |
| pointbypointstructure |  | slitType |  |  |
| process |  | stoppingpowerdefaultType |  |  |
| reaction |  | totalabsorptioncrosssectionsType |  |  |
| reactionlist |  | totalabsorptioncrosssectionType |  |  |
| reactions |  | transitionratiosType |  |  |
| repository |  | usersType |  |  |
| resolutionparameters |  |  |  |  |
| roughness |  |  |  |  |
| sample |  |  |  |  |
| simulation |  |  |  |  |
| simulations |  |  |  |  |
| spectra |  |  |  |  |
| spectrum |  |  |  |  |
| stoppingpower |  |  |  |  |
| stoppingpowers |  |  |  |  |
| structure |  |  |  |  |
| tof |  |  |  |  |
| updatetimes |  |  |  |  |

element amplifier

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes amplifiertype pulseshape shapingtime risetime flattoptime pur purtime |
| used by | element electronics |
| annotation | documentation Some parameters that describe the amplifier and are needed e.g. for pileup calculations are given here. |

element amplifier/amplifiertype

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | amplifiertypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration analogue enumeration DSP enumeration other |

element amplifier/pulseshape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | pulseshapeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration Gaussian enumeration trapezoidal enumeration triangular enumeration other |

element amplifier/shapingtime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | timevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element amplifier/risetime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | timevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element amplifier/flattoptime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | timevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element amplifier/pur

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | purType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration on enumeration off enumeration none |

element amplifier/purtime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | timevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element attributes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes idfversion filename createtime updatetimes |
| used by | element idf |
| annotation | documentation Tese are attributes of the IDF file, including version of IDF that this file conforms to, name of the IDF file, date file was created, any number of dates that the file was update |

element attributes/idfversion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 content simple |

element attributes/filename

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element attributes/createtime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | dateType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element beam

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes beamparticle beamZ beammass beamenergy beamenergyspread beamchargestate beamfluence beamcurrent beamangularspread beamshape slitsbeforesample beamfoil |
| used by | element beamrepository group experimental |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-beam . @ref¦@id unique beamparticle . @ref¦idf:beamparticle unique beamZ . @ref¦idf:beamZ unique beammass . @ref¦idf:beammass unique beamenergy . @ref¦idf:beamenergy unique beamenergyspread . @ref¦idf:beamenergyspread unique beamfluence . @ref¦idf:beamfluence unique beamcurrent . @ref¦idf:beamcurrent unique beamangularspread . @ref¦idf:beamangularspread unique beamshape . @ref¦idf:beamshape/idf:shape unique beamfoil . @ref¦idf:beamfoil/idf:foildistancetosample |
| annotation | documentation The beam data group defines the experimental conditions of the beam before hitting the sample, including beam energy, energy spread, charge state, shape, any slits and foils, current |

element beam/beamparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element beam/beamZ

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:positiveInteger |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element beam/beammass

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | massvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element beam/beamenergy

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units energyunitsType required |

element beam/beamenergyspread

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyvaluespreadType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units energyunitsType required mode modeType required |

element beam/beamchargestate

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simplesimulationType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element beam/beamfluence

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fluencevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element beam/beamcurrent

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | currentvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element beam/beamangularspread

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | anglevaluespreadType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required mode modeType required |

element beam/beamshape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape2dType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes shape l1 l2 |

element beam/slitsbeforesample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | slitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes slit |

element beam/beamfoil

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | foilType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes foildistancetosample foillayers |

element beamrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes beam |
| used by | element repository |
| annotation | documentation If, for instance, the same beam and energy was used for many samples, it can be defined here only once, instead of repeating the same information in every sample |

element calibrationparameters

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes calibrationparameter |
| used by | element energycalibration |

element calibrationparameters/calibrationparameter

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energycalibrationType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional units energycalibrationsunitsType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

element calibrations

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detectorefficiencies detectorresolutions energycalibrations |
| used by | group experimental |
| annotation | documentation calibrations includes e.g. detector efficiency and resolution, and energy calibration. Often, samples measured in one batch share these parameters Detector efficiencies and energy calibrations could also be given in the “detection” group. However, the calibrations depend not only on the aparatus, but also on the detected particle |

element calibrationsrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detectorefficiency detectorresolution energycalibration |
| used by | element repository |
| annotation | documentation calibrations includes e.g. detector efficiency and resolution, and energy calibration. Often, samples measured in one batch share these parameters |

element crosssection

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes crosssectionframe crosssectiontype reaction crosssectionoverride crosssectionfile crosssectiondata |
| used by | element crosssections |
| annotation | documentation This data group contains one given cross section for one given simulation, including any override of the default |

element crosssection/crosssectionframe

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | crosssectionframeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration cm enumeration lab |

element crosssection/crosssectiontype

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | crosssectiontypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration total enumeration differential |

element crosssection/crosssectionoverride

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | crosssectiondefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes Rutherford screening computercode |

element crosssection/crosssectionfile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element crosssection/crosssectiondata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledatacrosssectionType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element crosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes crosssection |
| used by | element physics |
| annotation | documentation This data group contains all the cross sections for one given simulation, including any override of the default |

element data

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes datamode channelmode simpledata complexdata linedata datafile |
| used by | element spectrum |
| annotation | documentation There are many different types of data that can be measured, and it is difficult to find a universal representation. The IDF supports most normal types of data and some exotic ones as well The complex datamode can be used to document practically any type of multidimensional data. |

element data/datamode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | datamodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration simple enumeration complex enumeration line enumeration file |

element data/channelmode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | channelmodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration left enumeration middle enumeration right enumeration other enumeration unknown |

element data/simpledata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledataType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element data/complexdata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | complexdataType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes datadimensions xaxes yaxes dataentries |

element data/linedata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | linedataType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes lineaxis yaxis yerroraxis line y yerror |

element data/datafile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element datadimensions

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes datadimensionx datadimensiony |
| used by | complexTypes complexdataType complexsimulationType |
| annotation | documentation For the complex data type, gives the dimensions of the data to be stored |

element datadimensions/datadimensionx

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:integer |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element datadimensions/datadimensiony

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:integer |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element dataentries

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes dataentry |
| used by | complexTypes complexdataType complexsimulationType |
| annotation | documentation For the complex data type, data is organised by many entries |

element dataentry

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes timestamp line dataitem |
| used by | element dataentries |
| annotation | documentation One given data entry, containing an unlimited amount of quantites, including a time stamp |

element dataentry/timestamp

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | dateType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element dataentry/line

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element dataentry/dataitem

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | anyrealvalueType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional mode modeType optional units xs:string optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

element detection

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes slitsaftersample stoppingfoil detector electronics |
| used by | element detectionrepository group experimental |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-detection . @ref¦@id unique stoppingfoil . @ref¦idf:stoppingfoil/idf:foildistancetosample unique detector-detectortype . @ref¦idf:detector/idf:detectortype unique detector-solidangle . @ref¦idf:detector/idf:solidangle unique electronics-amplifiertype . @ref¦idf:electronics/idf:amplifier/idf:amplifiertype unique electronics-shapingtime . @ref¦idf:electronics/idf:amplifier/idf:shapingtime unique electronics-purtime . @ref¦idf:electronics/idf:amplifier/idf:purtime unique electronics-pur . @ref¦idf:electronics/idf:amplifier/idf:pur |
| annotation | documentation detection includes everything that comes after the sample, such as slits, foils, detector, electronics. Instead of defining here, a reference to a detection data group in the repository can be made |

element detection/slitsaftersample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | slitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes slit |

element detection/stoppingfoil

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | foilType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes foildistancetosample foillayers |

element detectionrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detection |
| used by | element repository |
| annotation | documentation detection includes everything that comes after the sample, such as slits, foils, detector, electronics. All samples measured with a given detector, where all these elements are the same, can reference a definition given here |

element detector

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detectortype solidangle detectorshape deadlayer entrancewindow detectorlayers tof distancedetectortosample |
| used by | element detection |
| annotation | documentation defines parameters of the detector |

element detector/detectortype

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | detectortypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration SSB enumeration SDD enumeration PINdiode enumeration Si(Li) enumeration Ge(Li) enumeration HPGe enumeration ToF enumeration EdE enumeration Bragg enumeration MagSpec enumeration ElSpec enumeration other |

element detector/solidangle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | solidanglevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element detector/detectorshape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape3dType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes shape l1 l2 l3 |

element detector/deadlayer

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layerType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layerthickness layeruniformity layerdensity layercrystalstructure layerelements layermolecules |

element detector/entrancewindow

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

element detector/detectorlayers

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

element detector/distancedetectortosample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element detectorefficiencies

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detectorefficiency |
| used by | element calibrations |
| annotation | documentation data group containing all detection efficiencies |

element detectorefficiency

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes efficiencyion efficiencymode efficiency lineefficiency |
| used by | elements calibrationsrepository detectorefficiencies |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-detectorefficiency . @ref¦@id unique efficiencyion . @ref¦idf:efficiencyion unique efficiencymode . @ref¦idf:efficiencymode |
| annotation | documentation data group containing one given detection efficiency |

element detectorefficiency/efficiencyion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element detectorefficiency/efficiencymode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | efficiencymodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration energy enumeration line enumeration other |

element detectorefficiency/efficiency

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledataefficiencyType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element detectorefficiency/lineefficiency

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | linedataType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes lineaxis yaxis yerroraxis line y yerror |

element detectorresolution

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes resolutionion resolutionparameters |
| used by | elements calibrationsrepository detectorresolutions |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-detectorresolution . @ref¦@id unique resolutionion . @ref¦idf:resolutionion |
| annotation | documentation energy resolution for one given detected particle, may be energy-dependent, given as a polynomial |

element detectorresolution/resolutionion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element detectorresolutions

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes detectorresolution |
| used by | element calibrations |
| annotation | documentation data group containing all energy resolution |

element electronics

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes amplifier |
| used by | element detection |
| annotation | documentation parameters referring to the electronics used, such as amplifier. |

element element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes name density |
| used by | element elements |
| annotation | documentation Defines a given element present in the sample |

element element/name

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element element/density

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | densityvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element elements

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes nelements element |
| used by | element elementsandmolecules |
| annotation | documentation The elements data group includes one element group per element present in the sample. This is redundant relative to molecules If both elements and molecules are present, care should be taken to ensure that they are consistent with each other. In case of inconsistency, elements it to be considered correct |

element elements/nelements

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:positiveInteger |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element elementsandmolecules

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes elements molecules |
| used by | elements elementsandmoleculesrepository sample |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-elementsandmolecules . @ref¦@id unique elements . @ref¦idf:elements/idf:nelements unique molecules . @ref¦idf:molecules/idf:nmolecules |
| annotation | documentation This data group is used to define what are the constituents of a sample, such as the elements present. Logical elements such as moledules can also be given |

element elementsandmoleculesrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes elementsandmolecules |
| used by | element repository |
| annotation | documentation Each elementsandmolecules tag defines one type of sample, i.e. it defines a set of elements or logical units. Similar samples can then all reference the information given here |

element energycalibration

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes calibrationion calibrationmode calibrationparameters |
| used by | elements calibrationsrepository energycalibrations |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-energycalibration . @ref¦@id unique calibrationion . @ref¦idf:calibrationion unique calibrationmode . @ref¦idf:calibrationmode |
| annotation | documentation data group containing one given energy calibration for one given detected particle |

element energycalibration/calibrationion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energycalibration/calibrationmode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | calibrationmodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration energy enumeration time enumeration PH enumeration other |

element energycalibrations

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes energycalibration |
| used by | element calibrations |
| annotation | documentation data group containing all energy calibrations |

element energyspread

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes ion ionchargestate targetelement energyspreadmode energyspreadoverride energyspreadfile energyspreaddata |
| used by | element energyspreads |
| annotation | documentation Defines energy spread options. This group is mainly a series of flags that inform where some effect that affect the energy spread of the beam are included in any calculation. Actual calculation requires a series of values taken from different places in the file |

element energyspread/ion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspread/ionchargestate

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:integer |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspread/targetelement

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspread/energyspreadmode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | stoppingmodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration total enumeration nuclear enumeration electronic |

element energyspread/energyspreadoverride

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyspreaddefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes energylossstraggling multiplescattering Dopplereffect beamangularspread geometricspread Tschalareffect computercode |

element energyspread/energyspreadfile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element energyspread/energyspreaddata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledataenergyspreadType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element energyspreads

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes energyspread |
| used by | element physics |
| annotation | documentation This data group contains all the energy spreads for one given simulation, including any override of the default |

element environment

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes temperature pressure |
| used by | element spectrum |
| annotation | documentation Data such as presure and temperature in the experimental data can be given here in a limited way. “temperature” and “pressure” are not extremely useful parameters. The “environment” group is here so users who have special requirements have a place to introduce user-specific environment-related tags. |

element environment/temperature

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | temperaturevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element environment/pressure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | pressurevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element equationoverlays

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes |
| used by | element layeredstructure |
| annotation | documentation This data group is empty in IDF, it is reserved for user-specific equation overlays to the layered structure defined |

element geometricspread

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes beamsize detectoraperture |
| used by | complexType energyspreaddefaultType |
| annotation | documentation Defines geometric spread options |

element geometricspread/beamsize

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element geometricspread/detectoraperture

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element geometry

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes geometrytype incidenceangle scatteringangle exitangle spot |
| used by | element geometryrepository group experimental |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-geometry . @ref¦@id unique geometrytype . @ref¦idf:geometrytype unique incidenceangle . @ref¦idf:incidenceangle unique scatteringangle . @ref¦idf:scatteringangle unique exitangle . @ref¦idf:exitangle unique spot . @ref¦idf:spot/idf:shape |
| annotation | documentation geometry defines only the basic quantities, such as scattering, incidence and exit angle, and beam spot. The experimental geometry is defined here as it pertains to scattering; the normal parameters considered in codes are used here, plus the definition of the spot in the sample. Further details on the geometry are found in the beam and instrument entries |

element geometry/geometrytype

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | geometrytypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration Cornell enumeration IBM enumeration general |

element geometry/incidenceangle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | anglevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element geometry/scatteringangle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | anglevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element geometry/exitangle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | anglevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element geometry/spot

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape2dType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes shape l1 l2 |

element geometryrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes geometry |
| used by | element repository |
| annotation | documentation geometry defines only the basic quantities, such as scattering, incidence and exit angle, and beam spot |

element idf

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes attributes repository sample |
| identity constraints | Name Refer Selector Field(s) unique id idf:repository/idf:elementsandmoleculesrepository/idf:elementsandmolecules¦ idf:repository/idf:beamrepository/idf:beam¦ idf:repository/idf:geometryrepository/idf:geometry¦ idf:repository/idf:instrumentrepository/idf:instrument¦ idf:repository/idf:detectionrepository/idf:detection¦ idf:repository/idf:calibrationsrepository/idf:detectorefficiency¦ idf:repository/idf:calibrationsrepository/idf:detectorresolution¦ idf:repository/idf:calibrationsrepository/idf:energycalibration @id keyref idref id idf:sample/idf:elementsandmolecules¦ idf:sample/idf:spectra/idf:spectrum/idf:beam¦ idf:sample/idf:spectra/idf:spectrum/idf:geometry¦ idf:sample/idf:spectra/idf:spectrum/idf:instrument¦ idf:sample/idf:spectra/idf:spectrum/idf:detection¦ idf:sample/idf:spectra/idf:spectrum/idf:detectorefficiency¦ idf:sample/idf:spectra/idf:spectrum/idf:detectorresolution¦ idf:sample/idf:spectra/idf:spectrum/idf:energycalibration @ref |
| annotation | documentation The root element of all IDF files must be idf. |

element instrument

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes ionsource accelerator beamline chamber sampleholder |
| used by | element instrumentrepository group experimental |
| attributes | Name Type Use Default Fixed annotation id xs:string optional ref xs:string optional |
| identity constraints | Name Refer Selector Field(s) unique refid-instrument . @ref¦@id unique ionsource . @ref¦idf:ionsource unique accelerator . @ref¦idf:accelerator unique beamline . @ref¦idf:beamline unique chamber . @ref¦idf:chamber unique sampleholder . @ref¦idf:sampleholder |
| annotation | documentation Instrument includes the accelerator, beam line and experimental chamber used. Instead of defining here, a reference to an instrument in the repository can be made |

element instrument/ionsource

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element instrument/accelerator

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element instrument/beamline

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element instrument/chamber

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element instrument/sampleholder

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element instrumentrepository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes instrument |
| used by | element repository |
| annotation | documentation Instrument includes the accelerator, beam line and experimental chamber used. All samples measured with the same setup can reference an instrument definition given here |

element layeredstructure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes nlayers layers equationoverlays roughness |
| used by | element structure |
| annotation | documentation A layered structure can be described withini this data group |

element layeredstructure/nlayers

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:positiveInteger |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element layeredstructure/layers

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

element layerelements

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes layerelement |
| used by | complexType layerType |
| annotation | documentation Defines the concentration of elements in the layers. This is redundant relative to layermolecules If both layerelements and layermolecules are present, care should be taken to ensure that they are consistent with each other. In case of inconsistency, layerelements it to be considered correct |

element layerelements/layerelement

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layerelementType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes name concentration |

element layermolecules

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes layermolecule |
| used by | complexType layerType |
| annotation | documentation Defines the concentration of logical elements in the layers. This is redundant relative to layerelements. If both layerelements and layermolecules are present, care should be taken to ensure that they are consistent with each other. In case of inconsistency, layerelements it to be considered correct |

element layermolecules/layermolecule

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layerelementType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes name concentration |

element log

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes realtime livetime deadtime starttime stoptime |
| used by | element spectrum |
| annotation | documentation Log data such as start and end times, live time and real time |

element log/realtime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:duration |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element log/livetime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:duration |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element log/deadtime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:duration |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element log/starttime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:dateTime |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element log/stoptime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:dateTime |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element molecule

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes name density |
| used by | element molecules |
| annotation | documentation Defines a given logical element present in the sample |

element molecule/name

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element molecule/density

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | densityvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element molecules

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes nmolecules molecule |
| used by | element elementsandmolecules |
| annotation | documentation The molecules data group includes one logical element (e.g. molecule or element) group per logical element (e.g. molecule or element) present in the sample. This is redundant relative to elements If both elements and molecules are present, care should be taken to ensure that they are consistent with each other. In case of inconsistency, elements it to be considered correct |

element molecules/nmolecules

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:positiveInteger |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element physics

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes crosssections stoppingpowers energyspreads PIXE |
| used by | element simulation |
| annotation | documentation the physics data group defines what is to be used for cross sections, stopping powers, energy spread, etc., including any override of the given defaults |

element physicsdefaults

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes crosssectiondefault stoppingpowerdefault energyspreaddefault PIXEdefault |
| used by | element process |
| annotation | documentation the physicsdefaults data group defines defaults to be used for cross sections, stopping powers, energy spread, etc. They can be overriden for any given simulation |

element physicsdefaults/crosssectiondefault

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | crosssectiondefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes Rutherford screening computercode |

element physicsdefaults/stoppingpowerdefault

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | stoppingpowerdefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes computercode |

element physicsdefaults/energyspreaddefault

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyspreaddefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes energylossstraggling multiplescattering Dopplereffect beamangularspread geometricspread Tschalareffect computercode |

element physicsdefaults/PIXEdefault

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | pixedefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes ionizationcrosssections Xrayproductioncrosssections totalabsorptioncrosssections massabsorptioncoeffficients fluorescenceyields costerkroningyields branchingratios transitionratios linewidths photoelectricionizationcrosssections jumpratios |

element PIXE

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes PIXEoverride totalabsorptioncrosssections massabsorptioncoeffficients fluorescenceyields costerkroningyields branchingratios transitionratios linewidths photoelectricionizationcrosssections jumpratios |
| used by | element physics |
| annotation | documentation This data group contains all parameters required for PIXE calculations |

element PIXE/PIXEoverride

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | pixedefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes ionizationcrosssections Xrayproductioncrosssections totalabsorptioncrosssections massabsorptioncoeffficients fluorescenceyields costerkroningyields branchingratios transitionratios linewidths photoelectricionizationcrosssections jumpratios |

element PIXE/totalabsorptioncrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | totalabsorptioncrosssectionsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes totalabsorptioncrosssection |

element PIXE/massabsorptioncoeffficients

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | massabsorptioncoeffficientsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes massabsorptioncoeffficient |

element PIXE/fluorescenceyields

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fluorescenceyieldsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes fluorescenceyield |

element PIXE/costerkroningyields

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | costerkroningyieldsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes costerkroningyield |

element PIXE/branchingratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | branchingratiosType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes branchingratio |

element PIXE/transitionratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | transitionratiosType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes transitionratio |

element PIXE/linewidths

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | linewidthsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes linewidth |

element PIXE/photoelectricionizationcrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | photoelectricionizationcrosssectionsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes photoelectricionizationcrosssection |

element PIXE/jumpratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | jumpratiosType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes jumpratio |

element pointbypointstructure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes element |
| used by | element structure |
| annotation | documentation A sample structure can be given by specifying a (depth/concentration) table for the elements This is the so-called “point by point” profile, in which for each element the yield in each channel in converted into a concentration by using the cross section. The depth is obtained by using calculated stopping power, either from the data directly, of if some elements are invisible, from an assumed structure (often iteratively). This method is popular for instance in HI-ERDA |

element pointbypointstructure/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | pbpelementType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes elementname pbp |
| used by | element elements |

element process

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes physicsdefaults simulations |
| used by | element spectrum |
| annotation | documentation here come the things that relate to the data analysis, including cross sections and stopping powers used, straggling models, simulations made, and anything else |

element reaction

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes initialtargetparticle incidentparticle exitparticle finaltargetparticle reactionQ |
| used by | elements crosssection reactionlist group simulationtypereaction |
| annotation | documentation Contains one given reaction of interest |

element reaction/initialtargetparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element reaction/incidentparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element reaction/exitparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element reaction/finaltargetparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element reaction/reactionQ

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units energyunitsType required |

element reactionlist

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes reaction |
| used by | element reactions |
| annotation | documentation Contains all reactions of interest |

element reactions

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes technique reactionlist |
| used by | element spectrum |
| annotation | documentation The reactions that occurr are listed in this data group. For RBS, ERDA, and PIXE, this is not strictly necessary, because the reactions can be deduced from kinematics. For NRA and NRP this is more important, even if some codes may have built-in lists of possible reactions. This could be a good place to specify cross section data to be used. However, conceptually these are separate things. One thing is reactions that occurr and particles detected that make up the data, a different thing is how this data is analysed. |

element reactions/technique

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | techniqueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration RBS enumeration ERDA enumeration NRA enumeration NRP enumeration PIXE enumeration other |

element repository

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes elementsandmoleculesrepository beamrepository geometryrepository instrumentrepository detectionrepository calibrationsrepository |
| used by | element idf |
| annotation | documentation DIfferent sections of experimental conditions can be defined in advance, to be referenced later. |

element resolutionparameters

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes resolutionparameter |
| used by | element detectorresolution |
| annotation | documentation one coefficient of the polynomial |

element resolutionparameters/resolutionparameter

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | resolutionparameterType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional mode modeType required units resolutionparameterunitsType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

element roughness

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes |
| used by | element layeredstructure |
| annotation | documentation This data group is empty in IDF, it is reserved for user-specific roughness description |

element sample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes elementsandmolecules structure spectra |
| used by | element idf |
| attributes | Name Type Use Default Fixed annotation id xs:string optional |
| annotation | documentation As many samples as desired can be included in one IDF file. Each sample corresponds to a new sample data group, that includes all the information about the sample, such as structure, any spectra measured (which can be more than one, or even none if it is a pure simulation), all experimental conditions for the different measurements, all calculations and simulations and their parameters |

element simulation

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes physics simulationtype initialtargetparticle targetlayer reaction datamode channelmode simpledata complexdata linedata datafile |
| used by | element simulations |
| annotation | documentation Contains one simulation made |

element simulation/simulationtype

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simulationtypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration total enumeration partialelement enumeration reaction |

element simulation/simpledata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simplesimulationType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element simulation/complexdata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | complexsimulationType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes datadimensions xaxes yaxes dataentries |

element simulation/linedata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | linesimulationType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xraylineaxis yieldaxis yielderroraxis xrayline yield yielderror |

element simulation/datafile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element simulations

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes simulation |
| used by | element process |
| annotation | documentation This data group contains all the simulations made |

element spectra

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes spectrum |
| used by | element sample |
| annotation | documentation The spectra data group contains one or more spectrum data groups |

element spectrum

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes log environment beam geometry instrument detection calibrations reactions data process |
| used by | element spectra |
| annotation | documentation The spectrum data group contains everyting referring to one given spectrum, including experimental conditions, data, and any simulations |

element stoppingpower

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes ion ionchargestate targetelement stoppingmode stoppingpoweroverride stoppingpowerfile stoppingpowerdata |
| used by | element stoppingpowers |
| annotation | documentation This data group contains one given stopping power for one given simulation, including any override of the default |

element stoppingpower/ion

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element stoppingpower/ionchargestate

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:integer |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element stoppingpower/targetelement

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element stoppingpower/stoppingmode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | stoppingmodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration total enumeration nuclear enumeration electronic |

element stoppingpower/stoppingpoweroverride

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | stoppingpowerdefaultType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes computercode |

element stoppingpower/stoppingpowerfile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element stoppingpower/stoppingpowerdata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledatastoppingpowerType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

element stoppingpowers

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes stoppingpower |
| used by | element physics |
| annotation | documentation This data group contains all the stopping powers for one given simulation, including any override of the default |

element structure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes crystalstructure layeredstructure pointbypointstructure |
| used by | element sample |
| annotation | documentation The structure data group is used to define the sample, in particular a given depth profile expressed for instance as a layered structure. Other methods are also allowed. Crystalline structure can also be given. The normal way of describing a sample structure is a layered description. A second way is the so-called “point by point” profile, in which for each element a table (depth, concentration) is calculated by directly converting the yield in each channel into a concentration. This second method is popular for instance in HI-ERDA |

element structure/crystalstructure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element tof

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes toflength toftimeresolution startfoil stoptfoil |
| used by | element detector |
| annotation | documentation defines parameters relevant for time of flight detectors |

element tof/toflength

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element tof/toftimeresolution

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | timevalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element tof/startfoil

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

element tof/stoptfoil

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

element updatetimes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| properties | content complex |
| children | users notes updatetime |
| used by | element attributes |
| annotation | documentation any number of “updatetime” tags can be given. |

element updatetimes/updatetime

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | dateType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content simple |

group experimental

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | beam geometry instrument detection calibrations |
| used by | element spectrum |
| annotation | documentation Experimental conditions are given in this group. They are separated in the data groups beam, geometry, instrument, detection, and calibrations |

group simulationtypepartialelement

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | initialtargetparticle targetlayer |
| used by | element simulation |
| annotation | documentation the structure of the simulated data is similar to what was specified in the "datamode" group of the "data" group. The x and y axes are exactly the same, but the simulation is for scattering off one single target element. This is useful to output in a simple way the calculate partial spectrum of a given element in RBS or ERDA. In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values. partialelementinlayer: if a given targetlayer is also specified, then the simulation is for the contribution of the given element in the specified layer onl |

element simulationtypepartialelement/initialtargetparticle

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 content simple |

element simulationtypepartialelement/targetlayer

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:integer |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

group simulationtypereaction

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | reaction datamode channelmode |
| used by | element simulation |
| annotation | documentation reaction: This is the fourth way to present a simulation. When simulationtype is "reaction", then one given reaction is simulated and presented. This becomes quite independent of the structure given in the "data" group, because the quantities can be all different. Suppose an RBS spectrum given in "data" as channel and total yield. Here, the simulated partial spectrum of one of the elements is to be presented as energy and elemental yield. Also, this can be used for a pure simulation, even for a complete spectrum; if in "reaction" only the incidentparticle is given, then all reactions are considered to be included |

element simulationtypereaction/datamode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | datamodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration simple enumeration complex enumeration line enumeration file |

element simulationtypereaction/channelmode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | channelmodeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration left enumeration middle enumeration right enumeration other enumeration unknown |

group simulationtypetotal

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| used by | element simulation |
| annotation | documentation structure of the simulated data is identical to what was specified in the "datamode" group of the "data" group. In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values |

group usersnotes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes |
| used by | elements amplifier attributes beam beamrepository calibrationparameters calibrations calibrationsrepository crosssection crosssections data datadimensions dataentries dataentry detection detectionrepository detector detectorefficiencies detectorefficiency detectorresolution detectorresolutions electronics element elements elementsandmolecules elementsandmoleculesrepository energycalibration energycalibrations energyspread energyspreads environment equationoverlays geometricspread geometry geometryrepository idf instrument instrumentrepository layeredstructure layerelements layermolecules log molecule molecules physics physicsdefaults PIXE pointbypointstructure process reaction reactionlist reactions repository resolutionparameters roughness sample simulation simulations spectra spectrum stoppingpower stoppingpowers structure tof updatetimes complexTypes atomicparameter1levelType atomicparameter2levelType atomicparameter2transitionType axesType axisconcentrationType axiscrosssectionType axisdepthType axisefficiencyType axisenergyspreadType axisenergyType axiserrorType axisstoppingpowerType axisType branchingratiosType codedatabaseType complexdataType complexsimulationType costerkroningyieldsType crosssectiondefaultType energyspreaddefaultType fileType fluorescenceyieldsType foilType jumpratiosType layerelementType layersType layerType linedataType linesimulationType linewidthsType massabsorptioncoeffficientsType massabsorptioncoeffficientType pbpelementType photoelectricionizationcrosssectionsType pixedefaultType shape2dType shape3dType simpledatacrosssectionType simpledatadepthconcentrationType simpledataefficiencyType simpledataenergyspreadType simpledatastoppingpowerType simpledataType simplesimulationType slitsType slitType stoppingpowerdefaultType totalabsorptioncrosssectionsType totalabsorptioncrosssectionType transitionratiosType |
| annotation | documentation Groups the users and notes elements |

element usersnotes/users

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | usersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | user |

element usersnotes/notes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | notesType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | note |

complexType atomicparameter1levelType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes element level value |
| used by | elements fluorescenceyieldsType/fluorescenceyield photoelectricionizationcrosssectionsType/photoelectricionizationcrosssection |
| annotation | documentation element, atomic level, and parameter value |

element atomicparameter1levelType/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:NMTOKEN |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| used by | element elements |

element atomicparameter1levelType/level

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | levelType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation pattern none pattern K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5 |

element atomicparameter1levelType/value

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | adimensionalType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional units derived by: unitsType required |

complexType atomicparameter2levelType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes element level1 level2 value |
| used by | elements branchingratiosType/branchingratio costerkroningyieldsType/costerkroningyield jumpratiosType/jumpratio |
| annotation | documentation element, two atomic levels, and parameter value |

element atomicparameter2levelType/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:NMTOKEN |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| used by | element elements |

element atomicparameter2levelType/level1

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | levelType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation pattern none pattern K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5 |

element atomicparameter2levelType/level2

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | levelType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation pattern none pattern K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5 |

element atomicparameter2levelType/value

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | adimensionalType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional units derived by: unitsType required |

complexType atomicparameter2transitionType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes element transition1 transition2 value |
| used by | elements linewidthsType/linewidth transitionratiosType/transitionratio |
| annotation | documentation element, two transitions, and parameter value |

element atomicparameter2transitionType/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:NMTOKEN |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| used by | element elements |

element atomicparameter2transitionType/transition1

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | transitionType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation pattern none pattern (K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5)\-(K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5) |

element atomicparameter2transitionType/transition2

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | transitionType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation pattern none pattern (K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5)\-(K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5) |

element atomicparameter2transitionType/value

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | adimensionalType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional units derived by: unitsType required |

complexType axesType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axis |
| used by | elements complexdataType/xaxes complexsimulationType/xaxes complexdataType/yaxes complexsimulationType/yaxes |
| annotation | documentation Contains any number of axes |

element axesType/axis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes axisname axisunit |

complexType axisconcentrationType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledatadepthconcentrationType/yaxis |
| annotation | documentation Contains one given concentration axis, with name and unit |

element axisconcentrationType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisconcentrationType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | concentrationunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration at% enumeration mol% enumeration wt% enumeration ug/g enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

complexType axiscrosssectionType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledatacrosssectionType/yaxis |
| annotation | documentation Contains one given cross section axis, with name and unit |

element axiscrosssectionType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axiscrosssectionType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | crosssectionunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration barn enumeration b enumeration mbarn enumeration mb enumeration cm2 enumeration cm2/mg enumeration cm2/ug enumeration cm2/(1e15at/cm2) enumeration rr enumeration other enumeration arbitrary enumeration none |

complexType axisdepthType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledatadepthconcentrationType/xaxis |
| annotation | documentation Contains one given depth axis, with name and unit |

element axisdepthType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisdepthType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | arealdensityorthicknessunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration other enumeration arbitrary enumeration none |

complexType axisefficiencyType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledataefficiencyType/yaxis |
| annotation | documentation Contains one given depth axis, with name and unit |

element axisefficiencyType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisefficiencyType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | efficiencyunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

complexType axisenergyspreadType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledataenergyspreadType/yaxis |
| annotation | documentation Contains one given energy spread axis, with name and unit |

element axisenergyspreadType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisenergyspreadType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration other enumeration arbitrary enumeration none |

complexType axisenergyType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | elements simpledataefficiencyType/xaxis simpledatacrosssectionType/xaxis simpledatastoppingpowerType/xaxis simpledataenergyspreadType/xaxis |
| annotation | documentation Contains one given depth axis, with name and unit |

element axisenergyType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisenergyType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | energyunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration other enumeration arbitrary enumeration none |

complexType axiserrorType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | elements simpledataType/xerroraxis simpledatadepthconcentrationType/xerroraxis simpledataefficiencyType/xerroraxis simpledatacrosssectionType/xerroraxis simpledatastoppingpowerType/xerroraxis simpledataenergyspreadType/xerroraxis simplesimulationType/xerroraxis simpledataType/yerroraxis simpledatadepthconcentrationType/yerroraxis simpledataefficiencyType/yerroraxis simpledatacrosssectionType/yerroraxis simpledatastoppingpowerType/yerroraxis simpledataenergyspreadType/yerroraxis simplesimulationType/yerroraxis |
| annotation | documentation Contains one given error axis, with name and unit |

element axiserrorType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | restriction of xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

element axiserrorType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | restriction of xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration same enumeration % enumeration fraction |

complexType axisstoppingpowerType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | element simpledatastoppingpowerType/yaxis |
| annotation | documentation Contains one given stopping power axis, with name and unit |

element axisstoppingpowerType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisstoppingpowerType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | stoppingpowerunitsType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration eV/A enumeration keV/A enumeration MeV/A enumeration eV/Angstrom enumeration keV/Angstrom enumeration MeV/Angstrom enumeration eV/nm enumeration keV/nm enumeration MeV/nm enumeration eV/um enumeration keV/um enumeration MeV/um enumeration eV/cm enumeration keV/cm enumeration MeV/cm enumeration eV/m enumeration keV/m enumeration MeV/m enumeration eV/(ug/cm2) enumeration keV/(ug/cm2) enumeration MeV/(ug/cm2) enumeration eV/(mg/cm2) enumeration keV/(mg/cm2) enumeration MeV/(mg/cm2) enumeration eV/(1e15at/cm2) enumeration keV/(1e15at/cm2) enumeration MeV/(1e15at/cm2) enumeration other enumeration arbitrary enumeration none |

complexType axisType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes axisname axisunit |
| used by | elements axesType/axis linedataType/lineaxis simpledataType/xaxis simplesimulationType/xaxis linesimulationType/xraylineaxis simpledataType/yaxis linedataType/yaxis simplesimulationType/yaxis linedataType/yerroraxis linesimulationType/yieldaxis linesimulationType/yielderroraxis |
| annotation | documentation Contains one given axis, with name and unit |

element axisType/axisname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element axisType/axisunit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType branchingratiosType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes branchingratio |
| used by | element PIXE/branchingratios |
| annotation | documentation Branching_ratios can be introduced for individual transitions between two atomic levels of given elements |

element branchingratiosType/branchingratio

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter2levelType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element level1 level2 value |

complexType codedatabaseType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes name version builddate releasedate |
| used by | elements pixedefaultType/branchingratios crosssectiondefaultType/computercode stoppingpowerdefaultType/computercode energyspreaddefaultType/computercode pixedefaultType/costerkroningyields pixedefaultType/fluorescenceyields pixedefaultType/ionizationcrosssections pixedefaultType/jumpratios pixedefaultType/linewidths massabsorptioncoeffficientType/massabsorptioncoeffficientdatabase pixedefaultType/massabsorptioncoeffficients pixedefaultType/photoelectricionizationcrosssections totalabsorptioncrosssectionType/totalabsorptioncrosssectiondatabase pixedefaultType/totalabsorptioncrosssections pixedefaultType/transitionratios pixedefaultType/Xrayproductioncrosssections |
| annotation | documentation Defines whether a computer code is used to calculate the cross section |

element codedatabaseType/name

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element codedatabaseType/version

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element codedatabaseType/builddate

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | dateType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element codedatabaseType/releasedate

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | dateType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType complexdataType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes datadimensions xaxes yaxes dataentries |
| used by | element data/complexdata |
| annotation | documentation Multidimensional data can be introduced with this data type. |

element complexdataType/xaxes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axesType |
| properties | isRef 0 content complex |
| children | users notes axis |

element complexdataType/yaxes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axesType |
| properties | isRef 0 content complex |
| children | users notes axis |

complexType complexsimulationType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes datadimensions xaxes yaxes dataentries |
| used by | element simulation/complexdata |
| annotation | documentation Similar to complexdataType, but the axis do not necessarily need to be given, since they may match what is in data. Nevertheless, they can be given if desired. |

element complexsimulationType/xaxes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axesType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axis |

element complexsimulationType/yaxes

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axesType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axis |

complexType costerkroningyieldsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes costerkroningyield |
| used by | element PIXE/costerkroningyields |
| annotation | documentation Coster-Kroning_yields can be introduced for individual transitions between two atomic levels of given elements |

element costerkroningyieldsType/costerkroningyield

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter2levelType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element level1 level2 value |

complexType crosssectiondefaultType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes Rutherford screening computercode |
| used by | elements physicsdefaults/crosssectiondefault crosssection/crosssectionoverride |
| annotation | documentation Type to define the default for cross sections |

element crosssectiondefaultType/Rutherford

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element crosssectiondefaultType/screening

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | screeningType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration none enumeration Andersen enumeration Ecuyer enumeration other |

element crosssectiondefaultType/computercode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

complexType energyspreaddefaultType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes energylossstraggling multiplescattering Dopplereffect beamangularspread geometricspread Tschalareffect computercode |
| used by | elements physicsdefaults/energyspreaddefault energyspread/energyspreadoverride |
| annotation | documentation Type to define the default for energy spread. This group is mainly a series of flags that inform where some effect that affect the energy spread of the beam are included in any calculation. Actual calculation requires a series of values taken from different places in the file |

element energyspreaddefaultType/energylossstraggling

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspreaddefaultType/multiplescattering

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspreaddefaultType/Dopplereffect

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspreaddefaultType/beamangularspread

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspreaddefaultType/Tschalareffect

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:boolean |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element energyspreaddefaultType/computercode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

complexType fileType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes filename fileformat filesource |
| used by | elements crosssection/crosssectionfile data/datafile simulation/datafile energyspread/energyspreadfile massabsorptioncoeffficientType/massabsorptioncoeffficientfile stoppingpower/stoppingpowerfile totalabsorptioncrosssectionType/totalabsorptioncrosssectionfile |
| annotation | documentation Defines a file reference |

element fileType/filename

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element fileType/fileformat

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element fileType/filesource

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType fluorescenceyieldsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes fluorescenceyield |
| used by | element PIXE/fluorescenceyields |
| annotation | documentation Fluorescence yields can be introduced for individual atomic levels of given elements |

element fluorescenceyieldsType/fluorescenceyield

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter1levelType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element level value |

complexType foilType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes foildistancetosample foillayers |
| used by | elements beam/beamfoil detection/stoppingfoil |
| annotation | documentation This type defines a multilayered foil, including distance to sample |

element foilType/foildistancetosample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element foilType/foillayers

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layersType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes layer |

complexType jumpratiosType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes jumpratio |
| used by | element PIXE/jumpratios |
| annotation | documentation Jump_ratios can be introduced for individual transitions between two atomic levels of given elements |

element jumpratiosType/jumpratio

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter2levelType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element level1 level2 value |

complexType layerelementType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes name concentration |
| used by | elements layerelements/layerelement layermolecules/layermolecule |
| annotation | documentation Type defining the concentration of one element in one layer |

element layerelementType/name

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element layerelementType/concentration

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | concentrationvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units concentrationunitsType required |

complexType layersType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes layer |
| used by | elements detector/detectorlayers detector/entrancewindow foilType/foillayers layeredstructure/layers tof/startfoil tof/stoptfoil |
| annotation | documentation Type defining layers |

element layersType/layer

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | layerType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes layerthickness layeruniformity layerdensity layercrystalstructure layerelements layermolecules |

complexType layerType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes layerthickness layeruniformity layerdensity layercrystalstructure layerelements layermolecules |
| used by | elements detector/deadlayer layersType/layer |
| annotation | documentation Type defining one given layer |

element layerType/layerthickness

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | arealdensityorthicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units arealdensityorthicknessunitsType required |

element layerType/layeruniformity

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | arealdensityorthicknessvaluespreadType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units arealdensityorthicknessunitsType required mode modeType required |

element layerType/layerdensity

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | densityvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element layerType/layercrystalstructure

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType linedataType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes lineaxis yaxis yerroraxis line y yerror |
| used by | elements data/linedata detectorefficiency/lineefficiency |
| annotation | documentation The data are given as a list of text values for x and numerical values for y. Useful for instance to input or output the yield for a given line. |

element linedataType/lineaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element linedataType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element linedataType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element linedataType/line

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | tokenlistType |
| properties | isRef 0 content simple |

element linedataType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element linedataType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType linesimulationType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xraylineaxis yieldaxis yielderroraxis xrayline yield yielderror |
| used by | element simulation/linedata |
| annotation | documentation Similar to linedataType |

element linesimulationType/xraylineaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element linesimulationType/yieldaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element linesimulationType/yielderroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element linesimulationType/xrayline

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | tokenlistType |
| properties | isRef 0 content simple |

element linesimulationType/yield

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element linesimulationType/yielderror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType linewidthsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes linewidth |
| used by | element PIXE/linewidths |
| annotation | documentation Linewidths can be introduced for individual transitions between two atomic levels of given elements.This is equivalent to transitionratios and is given as alternative, one or the othe |

element linewidthsType/linewidth

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter2transitionType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element transition1 transition2 value |

complexType massabsorptioncoeffficientsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes massabsorptioncoeffficient |
| used by | element PIXE/massabsorptioncoeffficients |
| annotation | documentation Mass absorption coeffficients can be introduced for individual elements |

element massabsorptioncoeffficientsType/massabsorptioncoeffficient

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | massabsorptioncoeffficientType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element massabsorptioncoeffficientdatabase massabsorptioncoeffficientfile massabsorptioncoeffficientdata |

complexType massabsorptioncoeffficientType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes element massabsorptioncoeffficientdatabase massabsorptioncoeffficientfile massabsorptioncoeffficientdata |
| used by | element massabsorptioncoeffficientsType/massabsorptioncoeffficient |
| annotation | documentation Mass absorption coeffficients for one given individual element |

element massabsorptioncoeffficientType/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:NMTOKEN |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| used by | element elements |

element massabsorptioncoeffficientType/massabsorptioncoeffficientdatabase

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element massabsorptioncoeffficientType/massabsorptioncoeffficientfile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element massabsorptioncoeffficientType/massabsorptioncoeffficientdata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledatacrosssectionType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

complexType notesType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | note |
| used by | element usersnotes/notes |
| annotation | documentation To introduce any other text information. every single group of tags can have the group “notes” just after the group “users”, where any information or comments can be given. Any number of tags “note” can be given. |

element notesType/note

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc unbounded content simple |

complexType pbpelementType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes elementname pbp |
| used by | element pointbypointstructure/element |
| annotation | documentation Type to define the point by point depth profile for one element |

element pbpelementType/elementname

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element pbpelementType/pbp

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledatadepthconcentrationType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

complexType photoelectricionizationcrosssectionsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes photoelectricionizationcrosssection |
| used by | element PIXE/photoelectricionizationcrosssections |
| annotation | documentation Photoelectric_ionization_cross_sections can be introduced for individual atomic levels of given elements |

element photoelectricionizationcrosssectionsType/photoelectricionizationcrosssection

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter1levelType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element level value |

complexType pixedefaultType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes ionizationcrosssections Xrayproductioncrosssections totalabsorptioncrosssections massabsorptioncoeffficients fluorescenceyields costerkroningyields branchingratios transitionratios linewidths photoelectricionizationcrosssections jumpratios |
| used by | elements physicsdefaults/PIXEdefault PIXE/PIXEoverride |
| annotation | documentation Type to define the default for PIXE required parameters. This group is mainly a series of text tags that inform what are the data bases used in calculation. Actual calculation requires knowledge by the codes about how to read, process and use the databases |

element pixedefaultType/ionizationcrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/Xrayproductioncrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/totalabsorptioncrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/massabsorptioncoeffficients

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/fluorescenceyields

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/costerkroningyields

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/branchingratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/transitionratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/linewidths

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/photoelectricionizationcrosssections

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element pixedefaultType/jumpratios

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

complexType shape2dType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes shape l1 l2 |
| used by | elements beam/beamshape geometry/spot |
| annotation | documentation Defines a 2 dimensional shape |

element shape2dType/shape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape2dtypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration circular enumeration square enumeration elliptical enumeration rectangular enumeration other |

element shape2dType/l1

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element shape2dType/l2

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

complexType shape3dType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes shape l1 l2 l3 |
| used by | elements detector/detectorshape slitType/slitshape |
| annotation | documentation Defines a 3 dimensional shape |

element shape3dType/shape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape2dtypeType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| facets | Kind Value annotation enumeration circular enumeration square enumeration elliptical enumeration rectangular enumeration other |

element shape3dType/l1

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element shape3dType/l2

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

element shape3dType/l3

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

complexType simpledatacrosssectionType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | elements crosssection/crosssectiondata massabsorptioncoeffficientType/massabsorptioncoeffficientdata totalabsorptioncrosssectionType/totalabsorptioncrosssectiondata |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledatacrosssectionType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisenergyType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatacrosssectionType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatacrosssectionType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiscrosssectionType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatacrosssectionType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatacrosssectionType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatacrosssectionType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledatacrosssectionType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatacrosssectionType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simpledatadepthconcentrationType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | element pbpelementType/pbp |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledatadepthconcentrationType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisdepthType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatadepthconcentrationType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatadepthconcentrationType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisconcentrationType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatadepthconcentrationType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatadepthconcentrationType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatadepthconcentrationType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledatadepthconcentrationType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatadepthconcentrationType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simpledataefficiencyType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | element detectorefficiency/efficiency |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledataefficiencyType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisenergyType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataefficiencyType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataefficiencyType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisefficiencyType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataefficiencyType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataefficiencyType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataefficiencyType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledataefficiencyType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataefficiencyType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simpledataenergyspreadType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | element energyspread/energyspreaddata |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledataenergyspreadType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisenergyType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataenergyspreadType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataenergyspreadType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisenergyspreadType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataenergyspreadType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataenergyspreadType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataenergyspreadType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledataenergyspreadType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataenergyspreadType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simpledatastoppingpowerType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | element stoppingpower/stoppingpowerdata |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledatastoppingpowerType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisenergyType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatastoppingpowerType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatastoppingpowerType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisstoppingpowerType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledatastoppingpowerType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledatastoppingpowerType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatastoppingpowerType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledatastoppingpowerType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledatastoppingpowerType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simpledataType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | element data/simpledata |
| annotation | documentation The data are given as a list of x and y, eventually with error axes as well. Names and units for each axis must be defined |

element simpledataType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 content complex |
| children | users notes axisname axisunit |

element simpledataType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simpledataType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simpledataType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simpledataType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType simplesimulationType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |
| used by | elements beam/beamchargestate simulation/simpledata |
| annotation | documentation Similar to simpledataType, but the axis do not necessarily need to be given, since they may match what is in data. Nevertheless, they can be given if desired. |

element simplesimulationType/xaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simplesimulationType/xerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simplesimulationType/yaxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axisType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simplesimulationType/yerroraxis

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | axiserrorType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes axisname axisunit |

element simplesimulationType/x

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simplesimulationType/xerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

element simplesimulationType/y

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 content simple |

element simplesimulationType/yerror

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | floatordoublelistType |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |

complexType slitsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes slit |
| used by | elements detection/slitsaftersample beam/slitsbeforesample |
| annotation | documentation This type includes multiple slits, each with given dimensions and a given distance to sample |

element slitsType/slit

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | slitType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes slitshape slitdistancetosample |

complexType slitType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes slitshape slitdistancetosample |
| used by | element slitsType/slit |
| annotation | documentation This type defines one given slit with given dimensions and a given distance to sample |

element slitType/slitshape

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | shape3dType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes shape l1 l2 l3 |

element slitType/slitdistancetosample

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | thicknessvalueType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required |

complexType stoppingpowerdefaultType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes computercode |
| used by | elements physicsdefaults/stoppingpowerdefault stoppingpower/stoppingpoweroverride |
| annotation | documentation Type to define the default for stopping powers |

element stoppingpowerdefaultType/computercode

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

complexType totalabsorptioncrosssectionsType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes totalabsorptioncrosssection |
| used by | element PIXE/totalabsorptioncrosssections |
| annotation | documentation Total absorption cross sections can be introduced for individual elements |

element totalabsorptioncrosssectionsType/totalabsorptioncrosssection

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | totalabsorptioncrosssectionType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element totalabsorptioncrosssectiondatabase totalabsorptioncrosssectionfile totalabsorptioncrosssectiondata |

complexType totalabsorptioncrosssectionType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes element totalabsorptioncrosssectiondatabase totalabsorptioncrosssectionfile totalabsorptioncrosssectiondata |
| used by | element totalabsorptioncrosssectionsType/totalabsorptioncrosssection |
| annotation | documentation Total absorption cross section for one given individual element |

element totalabsorptioncrosssectionType/element

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:NMTOKEN |
| properties | isRef 0 minOcc 0 maxOcc 1 content simple |
| used by | element elements |

element totalabsorptioncrosssectionType/totalabsorptioncrosssectiondatabase

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | codedatabaseType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes name version builddate releasedate |

element totalabsorptioncrosssectionType/totalabsorptioncrosssectionfile

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | fileType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes filename fileformat filesource |

element totalabsorptioncrosssectionType/totalabsorptioncrosssectiondata

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | simpledatacrosssectionType |
| properties | isRef 0 minOcc 0 maxOcc 1 content complex |
| children | users notes xaxis xerroraxis yaxis yerroraxis x xerror y yerror |

complexType transitionratiosType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | users notes transitionratio |
| used by | element PIXE/transitionratios |
| annotation | documentation Transition_ratios can be introduced for individual transitions between two atomic levels of given elements. This is equivalent to linewidths and is given as alternative, one or the other |

element transitionratiosType/transitionratio

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | atomicparameter2transitionType |
| properties | isRef 0 minOcc 0 maxOcc unbounded content complex |
| children | users notes element transition1 transition2 value |

complexType usersType

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| children | user |
| used by | element usersnotes/users |
| annotation | documentation To introduce information on users. every single group of tags can start with the group “users”, where information on e.g. sample owner, experimentalist, data analyst can be given. Any number of tags “user” can be given. |

element usersType/user

| diagram |  |
| --- | --- |
| namespace | http://schemas.itn.pt/idf |
| type | xs:string |
| properties | isRef 0 minOcc 0 maxOcc unbounded content simple |

simpleType amplifiertypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element amplifier/amplifiertype |
| facets | Kind Value annotation enumeration analogue enumeration DSP enumeration other |
| annotation | documentation defines the type of amplifier |

simpleType calibrationmodeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element energycalibration/calibrationmode |
| facets | Kind Value annotation enumeration energy enumeration time enumeration PH enumeration other |
| annotation | documentation specifies how the calibration is given - energy, time, pulse height, other |

simpleType channelmodeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | elements data/channelmode simulationtypereaction/channelmode |
| facets | Kind Value annotation enumeration left enumeration middle enumeration right enumeration other enumeration unknown |
| annotation | documentation flag defining what a channel is. Values left, middle or right for indicate that the channel number gives the left, middle or right edge of a channel. Example: With an offset of 0 keV and 1 keV/channel channel #1 is from 1 – 2 keV for left, from 0 – 1 keV for right, and from 0.5 – 1.5 keV for middle. In the case of non-equidistant energy steps only left and right are allowed, because the original channel edges cannot be reconstructed if only the middle of each channel is given. |

simpleType crosssectionframeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element crosssection/crosssectionframe |
| facets | Kind Value annotation enumeration cm enumeration lab |
| annotation | documentation Defines the frame of reference where the cross section is given |

simpleType crosssectiontypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element crosssection/crosssectiontype |
| facets | Kind Value annotation enumeration total enumeration differential |
| annotation | documentation Defines the cross section type (total or differential) |

simpleType datamodeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | elements data/datamode simulationtypereaction/datamode |
| facets | Kind Value annotation enumeration simple enumeration complex enumeration line enumeration file |
| annotation | documentation Flag defining the type of data that follows (simple, complex, line) |

simpleType detectortypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element detector/detectortype |
| facets | Kind Value annotation enumeration SSB enumeration SDD enumeration PINdiode enumeration Si(Li) enumeration Ge(Li) enumeration HPGe enumeration ToF enumeration EdE enumeration Bragg enumeration MagSpec enumeration ElSpec enumeration other |
| annotation | documentation defines the detector type |

simpleType efficiencymodeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element detectorefficiency/efficiencymode |
| facets | Kind Value annotation enumeration energy enumeration line enumeration other |
| annotation | documentation specifies how the efficiency is given - for specific energies, or for specific x-ray lines |

simpleType geometrytypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element geometry/geometrytype |
| facets | Kind Value annotation enumeration Cornell enumeration IBM enumeration general |
| annotation | documentation defines the type of geometry |

simpleType pulseshapeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element amplifier/pulseshape |
| facets | Kind Value annotation enumeration Gaussian enumeration trapezoidal enumeration triangular enumeration other |
| annotation | documentation defines the pulse shape |

simpleType purType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element amplifier/pur |
| facets | Kind Value annotation enumeration on enumeration off enumeration none |
| annotation | documentation whether PUR system is on, off, or absent |

simpleType screeningType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element crosssectiondefaultType/screening |
| facets | Kind Value annotation enumeration none enumeration Andersen enumeration Ecuyer enumeration other |
| annotation | documentation Defines whether electron screening is computed |

simpleType shape2dtypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | elements shape2dType/shape shape3dType/shape |
| facets | Kind Value annotation enumeration circular enumeration square enumeration elliptical enumeration rectangular enumeration other |
| annotation | documentation Defines the type of a 2D shape |

simpleType simulationtypeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element simulation/simulationtype |
| facets | Kind Value annotation enumeration total enumeration partialelement enumeration reaction |
| annotation | documentation Defines what type of simulation is given. total: structure of the simulated data is identical to what was specified in the "datamode" group of the "data" group. In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values partialelement: the structure of the simulated data is similar to what was specified in the "datamode" group of the "data" group. The x and y axes are exactly the same, but the simulation is for scattering off one single target element. This is useful to output in a simple way the calculate partial spectrum of a given element in RBS or ERDA. In principle, the x entries should be exactly the same as given in the "data" group; and to write them here again is simple redundancy, for the purpose of ease of extracting the simulated data together with the x axes values. If a given targetlayer is also specified, then the simulation is for the contribution of the given element in the specified layer only. reaction: This is the fourth way to present a simulation. When simulationtype is "reaction", then one given reaction is simulated and presented. This becomes quite independent of the structure given in the "data" group, because the quantities can be all different. Suppose an RBS spectrum given in "data" as channel and total yield. Here, the simulated partial spectrum of one of the elements is to be presented as energy and elemental yield. Also, this can be used for a pure simulation, even for a complete spectrum; if in "reaction" only the incidentparticle is given, then all reactions are considered to be included |

simpleType stoppingmodeType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | elements energyspread/energyspreadmode stoppingpower/stoppingmode |
| facets | Kind Value annotation enumeration total enumeration nuclear enumeration electronic |
| annotation | documentation Defines whether the given stopping is total, nuclear or electronic |

simpleType techniqueType

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| type | restriction of xs:string |
| used by | element reactions/technique |
| facets | Kind Value annotation enumeration RBS enumeration ERDA enumeration NRA enumeration NRP enumeration PIXE enumeration other |
| annotation | documentation Defines the technique, such as RBS, NRA, etc technique considered, options are: RBS - including forward scattering and non-Rutherford elastic scattering ERDA - no matter what the beam NRA - for non-resonant i.e. particle-particle reactions, in which a single beam energy is used and an energy spectrum is collected NRP - for resonant reactions, in which the result is the total yield for normally a sharp resonance, and often an excitation function is measured using a range of initial beam energies. This includes PIGE and RNRA. PIXE - no matter what the beam other This is the main technique. Note however, for instance in ERDA, the forward scattered primary beam can also be detected. |

attributeGroup id

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| used by | elements beam detection detectorefficiency detectorresolution elementsandmolecules energycalibration geometry instrument sample |
| attributes | Name Type Use Default Fixed annotation id xs:string optional |
| annotation | documentation the id attribute to identify a given data group in the repository |

attribute id/@id

| type | xs:string |
| --- | --- |
| properties | isRef 0 form unqualified use optional |

attributeGroup ref

| namespace | http://schemas.itn.pt/idf |
| --- | --- |
| used by | elements beam detection detectorefficiency detectorresolution elementsandmolecules energycalibration geometry instrument |
| attributes | Name Type Use Default Fixed annotation ref xs:string optional |
| annotation | documentation the ref attribute to refer to a given data group in the repository |

attribute ref/@ref

| type | xs:string |
| --- | --- |
| properties | isRef 0 form unqualified use optional |

XML Schema documentation generated by XMLSpy Schema Editor http://www.altova.com/xmlspy

Appendix II: XMLSpy documentation for IDFunitsv1.xsd

Schema IDFunitsv1.xsd

| schema location: | D:\NDF\Nuno\IBA_IDF\IDFunitsv1.xsd |
| --- | --- |
| attribute form default: |  |
| element form default: |  |

| Complex types | Simple types |
| --- | --- |
| adimensionalType | arealdensityorthicknessunitsType |
| anglevaluespreadType | concentrationunitsType |
| anglevalueType | crosssectionunitsType |
| anyrealvalueType | dateType |
| arealdensityorthicknessvaluespreadType | efficiencyunitsType |
| arealdensityorthicknessvalueType | energycalibrationsunitsType |
| arealdensityvalueType | energyunitsType |
| atomicnumbervalueType | floatordoublelistType |
| chargevalueType | floatordoubleType |
| concentrationvalueType | levelType |
| crosssectionvalueType | modeType |
| currentvalueType | quantityType |
| densityvalueType | resolutionparameterunitsType |
| efficiencyType | stoppingpowerunitsType |
| energycalibrationType | tokenlistType |
| energyvaluespreadType | transitionType |
| energyvalueType | unitsType |
| fluencevalueType | yieldunitsType |
| massvalueType |  |
| othervalueType |  |
| pressurevalueType |  |
| realvaluespreadType |  |
| realvalueType |  |
| resolutionparameterType |  |
| solidanglevalueType |  |
| stoppingpowervalueType |  |
| temperaturevalueType |  |
| thicknessvalueType |  |
| timevalueType |  |
| yieldType |  |

complexType adimensionalType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute adimensionalType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration none |

complexType anglevaluespreadType

| diagram |  |
| --- | --- |
| type | extension of anglevalueType |
| properties | base anglevalueType |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units derived by: unitsType required mode modeType required |

attribute anglevaluespreadType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

complexType anglevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| used by | complexType anglevaluespreadType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute anglevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration angle |

attribute anglevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration degree enumeration rad enumeration mrad enumeration other enumeration arbitrary enumeration none |

complexType anyrealvalueType

| diagram |  |
| --- | --- |
| type | extension of floatordoubleType |
| properties | base floatordoubleType |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional mode modeType optional units xs:string optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute anyrealvalueType/@quantity

| type | xs:NMTOKEN |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

attribute anyrealvalueType/@units

| type | xs:string |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@uncertainty

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@uncertaintyA

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@uncertaintyB

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@uncertaintyplus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute anyrealvalueType/@uncertaintyminus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

complexType arealdensityorthicknessvaluespreadType

| diagram |  |
| --- | --- |
| type | extension of arealdensityorthicknessvalueType |
| properties | base arealdensityorthicknessvalueType |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units arealdensityorthicknessunitsType required mode modeType required |

attribute arealdensityorthicknessvaluespreadType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

complexType arealdensityorthicknessvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| used by | complexType arealdensityorthicknessvaluespreadType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units arealdensityorthicknessunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute arealdensityorthicknessvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration arealdensity enumeration thickness enumeration length |

attribute arealdensityorthicknessvalueType/@units

| type | arealdensityorthicknessunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration other enumeration arbitrary enumeration none |

complexType arealdensityvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute arealdensityvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration arealdensity |

attribute arealdensityvalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration other enumeration arbitrary enumeration none |

complexType atomicnumbervalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute atomicnumbervalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration atomicnumber |

attribute atomicnumbervalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration other enumeration arbitrary enumeration none |

complexType chargevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute chargevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration charge |

attribute chargevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration q enumeration other enumeration arbitrary enumeration none |

complexType concentrationvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units concentrationunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute concentrationvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration concentration |

attribute concentrationvalueType/@units

| type | concentrationunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration at% enumeration mol% enumeration wt% enumeration ug/g enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

complexType crosssectionvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units crosssectionunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute crosssectionvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration crosssection |

attribute crosssectionvalueType/@units

| type | crosssectionunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration barn enumeration b enumeration mbarn enumeration mb enumeration cm2 enumeration cm2/mg enumeration cm2/ug enumeration cm2/(1e15at/cm2) enumeration rr enumeration other enumeration arbitrary enumeration none |

complexType currentvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute currentvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration current |

attribute currentvalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration nA enumeration nAmpere enumeration Ampere enumeration other enumeration arbitrary enumeration none |

complexType densityvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute densityvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration density |

attribute densityvalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration g/cm3 enumeration 1e22at/cm3 enumeration other enumeration arbitrary enumeration none |

complexType efficiencyType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units efficiencyunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute efficiencyType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration efficiency |

attribute efficiencyType/@units

| type | efficiencyunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

complexType energycalibrationType

| diagram |  |
| --- | --- |
| type | extension of floatordoubleType |
| properties | base floatordoubleType |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional units energycalibrationsunitsType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute energycalibrationType/@quantity

| type | xs:NMTOKEN |
| --- | --- |
| properties | isRef 0 use optional |

attribute energycalibrationType/@units

| type | energycalibrationsunitsType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation pattern [kM]?eV(/channel(^\d+)?)? |

attribute energycalibrationType/@uncertainty

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute energycalibrationType/@uncertaintyA

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute energycalibrationType/@uncertaintyB

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute energycalibrationType/@uncertaintyplus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute energycalibrationType/@uncertaintyminus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

complexType energyvaluespreadType

| diagram |  |
| --- | --- |
| type | extension of energyvalueType |
| properties | base energyvalueType |
| attributes | Name Type Use Default Fixed annotation uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional quantity derived by: quantityType optional units energyunitsType required mode modeType required |

attribute energyvaluespreadType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

complexType energyvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| used by | complexType energyvaluespreadType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units energyunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute energyvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration energy |

attribute energyvalueType/@units

| type | energyunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration other enumeration arbitrary enumeration none |

complexType fluencevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute fluencevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration fluence |

attribute fluencevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration uC enumeration puC enumeration C enumeration pC enumeration uCoulomb enumeration puCoulomb enumeration Coulomb enumeration pCoulomb enumeration #particles enumeration other enumeration arbitrary enumeration none |

complexType massvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute massvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration mass |

attribute massvalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration amu enumeration g enumeration kg enumeration other enumeration arbitrary enumeration none |

complexType othervalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute othervalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration other |

attribute othervalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration other enumeration arbitrary enumeration none |

complexType pressurevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute pressurevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration pressure |

attribute pressurevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration atm enumeration bar enumeration mbar enumeration Torr enumeration mTorr enumeration mmHg enumeration Pa enumeration other enumeration arbitrary enumeration none |

complexType realvaluespreadType

| diagram |  |
| --- | --- |
| type | extension of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional units unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional mode modeType required |

attribute realvaluespreadType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

complexType realvalueType

| diagram |  |
| --- | --- |
| type | extension of floatordoubleType |
| properties | base floatordoubleType |
| used by | complexTypes adimensionalType anglevalueType arealdensityorthicknessvalueType arealdensityvalueType atomicnumbervalueType chargevalueType concentrationvalueType crosssectionvalueType currentvalueType densityvalueType efficiencyType energyvalueType fluencevalueType massvalueType othervalueType pressurevalueType realvaluespreadType solidanglevalueType stoppingpowervalueType temperaturevalueType thicknessvalueType timevalueType yieldType |
| attributes | Name Type Use Default Fixed annotation quantity quantityType optional units unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute realvalueType/@quantity

| type | quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration efficiency enumeration time enumeration yield enumeration energy enumeration density enumeration thickness enumeration length enumeration arealdensity enumeration concentration enumeration crosssection enumeration stoppingpower enumeration charge enumeration mass enumeration atomicnumber enumeration current enumeration fluence enumeration angle enumeration solidangle enumeration temperature enumeration pressure enumeration other |

attribute realvalueType/@units

| type | unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration s enumeration ms enumeration ns enumeration us enumeration counts enumeration counts/(uCmg/cm2) enumeration counts/(uC1e15at/cm2) enumeration counts/(uCug/cm2) enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration g/cm3 enumeration 1e22at/cm3 enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration at% enumeration mol% enumeration wt% enumeration ug/g enumeration fraction enumeration relative enumeration barn enumeration b enumeration mbarn enumeration mb enumeration cm2 enumeration cm2/mg enumeration cm2/ug enumeration cm2/(1e15at/cm2) enumeration rr enumeration eV/A enumeration keV/A enumeration MeV/A enumeration eV/Angstrom enumeration keV/Angstrom enumeration MeV/Angstrom enumeration eV/nm enumeration keV/nm enumeration MeV/nm enumeration eV/um enumeration keV/um enumeration MeV/um enumeration eV/cm enumeration keV/cm enumeration MeV/cm enumeration eV/m enumeration keV/m enumeration MeV/m enumeration eV/(ug/cm2) enumeration keV/(ug/cm2) enumeration MeV/(ug/cm2) enumeration eV/(mg/cm2) enumeration keV/(mg/cm2) enumeration MeV/(mg/cm2) enumeration eV/(1e15at/cm2) enumeration keV/(1e15at/cm2) enumeration MeV/(1e15at/cm2) enumeration q enumeration amu enumeration g enumeration kg enumeration nA enumeration nAmpere enumeration Ampere enumeration uC enumeration puC enumeration C enumeration pC enumeration uCoulomb enumeration puCoulomb enumeration Coulomb enumeration pCoulomb enumeration #particles enumeration degree enumeration rad enumeration mrad enumeration sr enumeration msr enumeration srad enumeration msrad enumeration C enumeration K enumeration atm enumeration bar enumeration mbar enumeration Torr enumeration mTorr enumeration mmHg enumeration Pa enumeration other enumeration arbitrary enumeration none |

attribute realvalueType/@uncertainty

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute realvalueType/@uncertaintyA

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute realvalueType/@uncertaintyB

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute realvalueType/@uncertaintyplus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute realvalueType/@uncertaintyminus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

complexType resolutionparameterType

| diagram |  |
| --- | --- |
| type | extension of floatordoubleType |
| properties | base floatordoubleType |
| attributes | Name Type Use Default Fixed annotation quantity xs:NMTOKEN optional mode modeType required units resolutionparameterunitsType optional uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute resolutionparameterType/@quantity

| type | xs:NMTOKEN |
| --- | --- |
| properties | isRef 0 use optional |

attribute resolutionparameterType/@mode

| type | modeType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

attribute resolutionparameterType/@units

| type | resolutionparameterunitsType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation pattern none pattern [kM]?eV(^-\d+)? |

attribute resolutionparameterType/@uncertainty

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute resolutionparameterType/@uncertaintyA

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute resolutionparameterType/@uncertaintyB

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute resolutionparameterType/@uncertaintyplus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

attribute resolutionparameterType/@uncertaintyminus

| type | floatordoubleType |
| --- | --- |
| properties | isRef 0 use optional |

complexType solidanglevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute solidanglevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration solidangle |

attribute solidanglevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration sr enumeration msr enumeration srad enumeration msrad enumeration other enumeration arbitrary enumeration none |

complexType stoppingpowervalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units stoppingpowerunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute stoppingpowervalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration stoppingpower |

attribute stoppingpowervalueType/@units

| type | stoppingpowerunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration eV/A enumeration keV/A enumeration MeV/A enumeration eV/Angstrom enumeration keV/Angstrom enumeration MeV/Angstrom enumeration eV/nm enumeration keV/nm enumeration MeV/nm enumeration eV/um enumeration keV/um enumeration MeV/um enumeration eV/cm enumeration keV/cm enumeration MeV/cm enumeration eV/m enumeration keV/m enumeration MeV/m enumeration eV/(ug/cm2) enumeration keV/(ug/cm2) enumeration MeV/(ug/cm2) enumeration eV/(mg/cm2) enumeration keV/(mg/cm2) enumeration MeV/(mg/cm2) enumeration eV/(1e15at/cm2) enumeration keV/(1e15at/cm2) enumeration MeV/(1e15at/cm2) enumeration other enumeration arbitrary enumeration none |

complexType temperaturevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute temperaturevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration temperature |

attribute temperaturevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration C enumeration K enumeration other enumeration arbitrary enumeration none |

complexType thicknessvalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute thicknessvalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration thickness enumeration length |

attribute thicknessvalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration other enumeration arbitrary enumeration none |

complexType timevalueType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units derived by: unitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute timevalueType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration time |

attribute timevalueType/@units

| type | restriction of unitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration s enumeration ms enumeration ns enumeration us enumeration other enumeration arbitrary enumeration none |

complexType yieldType

| diagram |  |
| --- | --- |
| type | restriction of realvalueType |
| properties | base realvalueType |
| attributes | Name Type Use Default Fixed annotation quantity derived by: quantityType optional units yieldunitsType required uncertainty floatordoubleType optional uncertaintyA floatordoubleType optional uncertaintyB floatordoubleType optional uncertaintyplus floatordoubleType optional uncertaintyminus floatordoubleType optional |

attribute yieldType/@quantity

| type | restriction of quantityType |
| --- | --- |
| properties | isRef 0 use optional |
| facets | Kind Value annotation enumeration yield |

attribute yieldType/@units

| type | yieldunitsType |
| --- | --- |
| properties | isRef 0 use required |
| facets | Kind Value annotation enumeration counts enumeration counts/(uCmg/cm2) enumeration counts/(uC1e15at/cm2) enumeration counts/(uCug/cm2) enumeration other enumeration arbitrary enumeration none |

simpleType arealdensityorthicknessunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute arealdensityorthicknessvalueType/@units |
| facets | Kind Value annotation enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration other enumeration arbitrary enumeration none |

simpleType concentrationunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute concentrationvalueType/@units |
| facets | Kind Value annotation enumeration at% enumeration mol% enumeration wt% enumeration ug/g enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

simpleType crosssectionunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute crosssectionvalueType/@units |
| facets | Kind Value annotation enumeration barn enumeration b enumeration mbarn enumeration mb enumeration cm2 enumeration cm2/mg enumeration cm2/ug enumeration cm2/(1e15at/cm2) enumeration rr enumeration other enumeration arbitrary enumeration none |

simpleType dateType

| type | union of (xs:date, xs:dateTime) |
| --- | --- |

simpleType efficiencyunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute efficiencyType/@units |
| facets | Kind Value annotation enumeration fraction enumeration relative enumeration other enumeration arbitrary enumeration none |

simpleType energycalibrationsunitsType

| type | restriction of xs:string |
| --- | --- |
| used by | attribute energycalibrationType/@units |
| facets | Kind Value annotation pattern [kM]?eV(/channel(^\d+)?)? |

simpleType energyunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute energyvalueType/@units |
| facets | Kind Value annotation enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration other enumeration arbitrary enumeration none |

simpleType floatordoublelistType

| type | list of floatordoubleType |
| --- | --- |

simpleType floatordoubleType

| type | union of (xs:float, xs:double) |
| --- | --- |
| used by | complexTypes anyrealvalueType energycalibrationType realvalueType resolutionparameterType simpleType floatordoublelistType attributes resolutionparameterType/@uncertainty energycalibrationType/@uncertainty realvalueType/@uncertainty anyrealvalueType/@uncertainty realvalueType/@uncertaintyA resolutionparameterType/@uncertaintyA anyrealvalueType/@uncertaintyA energycalibrationType/@uncertaintyA resolutionparameterType/@uncertaintyB anyrealvalueType/@uncertaintyB realvalueType/@uncertaintyB energycalibrationType/@uncertaintyB resolutionparameterType/@uncertaintyminus energycalibrationType/@uncertaintyminus realvalueType/@uncertaintyminus anyrealvalueType/@uncertaintyminus energycalibrationType/@uncertaintyplus realvalueType/@uncertaintyplus resolutionparameterType/@uncertaintyplus anyrealvalueType/@uncertaintyplus |

simpleType levelType

| type | restriction of xs:string |
| --- | --- |
| facets | Kind Value annotation pattern none pattern K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5 |

simpleType modeType

| type | restriction of xs:string |
| --- | --- |
| used by | attributes anyrealvalueType/@mode realvaluespreadType/@mode anglevaluespreadType/@mode arealdensityorthicknessvaluespreadType/@mode energyvaluespreadType/@mode resolutionparameterType/@mode |
| facets | Kind Value annotation enumeration FWHM enumeration sigma enumeration variance |

simpleType quantityType

| type | restriction of xs:NMTOKEN |
| --- | --- |
| used by | attributes energyvalueType/@quantity thicknessvalueType/@quantity arealdensityvalueType/@quantity arealdensityorthicknessvalueType/@quantity concentrationvalueType/@quantity crosssectionvalueType/@quantity stoppingpowervalueType/@quantity chargevalueType/@quantity massvalueType/@quantity atomicnumbervalueType/@quantity currentvalueType/@quantity fluencevalueType/@quantity anglevalueType/@quantity solidanglevalueType/@quantity temperaturevalueType/@quantity pressurevalueType/@quantity densityvalueType/@quantity timevalueType/@quantity efficiencyType/@quantity othervalueType/@quantity yieldType/@quantity realvalueType/@quantity |
| facets | Kind Value annotation enumeration efficiency enumeration time enumeration yield enumeration energy enumeration density enumeration thickness enumeration length enumeration arealdensity enumeration concentration enumeration crosssection enumeration stoppingpower enumeration charge enumeration mass enumeration atomicnumber enumeration current enumeration fluence enumeration angle enumeration solidangle enumeration temperature enumeration pressure enumeration other |

simpleType resolutionparameterunitsType

| type | restriction of xs:string |
| --- | --- |
| used by | attribute resolutionparameterType/@units |
| facets | Kind Value annotation pattern none pattern [kM]?eV(^-\d+)? |

simpleType stoppingpowerunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute stoppingpowervalueType/@units |
| facets | Kind Value annotation enumeration eV/A enumeration keV/A enumeration MeV/A enumeration eV/Angstrom enumeration keV/Angstrom enumeration MeV/Angstrom enumeration eV/nm enumeration keV/nm enumeration MeV/nm enumeration eV/um enumeration keV/um enumeration MeV/um enumeration eV/cm enumeration keV/cm enumeration MeV/cm enumeration eV/m enumeration keV/m enumeration MeV/m enumeration eV/(ug/cm2) enumeration keV/(ug/cm2) enumeration MeV/(ug/cm2) enumeration eV/(mg/cm2) enumeration keV/(mg/cm2) enumeration MeV/(mg/cm2) enumeration eV/(1e15at/cm2) enumeration keV/(1e15at/cm2) enumeration MeV/(1e15at/cm2) enumeration other enumeration arbitrary enumeration none |

simpleType tokenlistType

| type | list of xs:NMTOKEN |
| --- | --- |

simpleType transitionType

| type | restriction of xs:string |
| --- | --- |
| facets | Kind Value annotation pattern none pattern (K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5)\-(K¦L[1-3]¦M[1-5]¦N[1-7]¦O[1-7]¦M4,5¦N2,3¦N6,7¦N6\(7\)¦O4,5) |

simpleType unitsType

| type | restriction of xs:string |
| --- | --- |
| used by | simpleTypes arealdensityorthicknessunitsType concentrationunitsType crosssectionunitsType efficiencyunitsType energyunitsType stoppingpowerunitsType yieldunitsType attributes realvalueType/@units othervalueType/@units timevalueType/@units densityvalueType/@units pressurevalueType/@units temperaturevalueType/@units solidanglevalueType/@units anglevalueType/@units fluencevalueType/@units currentvalueType/@units atomicnumbervalueType/@units massvalueType/@units chargevalueType/@units arealdensityvalueType/@units thicknessvalueType/@units adimensionalType/@units |
| facets | Kind Value annotation enumeration s enumeration ms enumeration ns enumeration us enumeration counts enumeration counts/(uCmg/cm2) enumeration counts/(uC1e15at/cm2) enumeration counts/(uCug/cm2) enumeration eV enumeration keV enumeration MeV enumeration eV^2 enumeration keV^2 enumeration MeV^2 enumeration g/cm3 enumeration 1e22at/cm3 enumeration A enumeration Angstrom enumeration nm enumeration um enumeration mm enumeration cm enumeration m enumeration ug/cm2 enumeration mg/cm2 enumeration 1e15at/cm2 enumeration at% enumeration mol% enumeration wt% enumeration ug/g enumeration fraction enumeration relative enumeration barn enumeration b enumeration mbarn enumeration mb enumeration cm2 enumeration cm2/mg enumeration cm2/ug enumeration cm2/(1e15at/cm2) enumeration rr enumeration eV/A enumeration keV/A enumeration MeV/A enumeration eV/Angstrom enumeration keV/Angstrom enumeration MeV/Angstrom enumeration eV/nm enumeration keV/nm enumeration MeV/nm enumeration eV/um enumeration keV/um enumeration MeV/um enumeration eV/cm enumeration keV/cm enumeration MeV/cm enumeration eV/m enumeration keV/m enumeration MeV/m enumeration eV/(ug/cm2) enumeration keV/(ug/cm2) enumeration MeV/(ug/cm2) enumeration eV/(mg/cm2) enumeration keV/(mg/cm2) enumeration MeV/(mg/cm2) enumeration eV/(1e15at/cm2) enumeration keV/(1e15at/cm2) enumeration MeV/(1e15at/cm2) enumeration q enumeration amu enumeration g enumeration kg enumeration nA enumeration nAmpere enumeration Ampere enumeration uC enumeration puC enumeration C enumeration pC enumeration uCoulomb enumeration puCoulomb enumeration Coulomb enumeration pCoulomb enumeration #particles enumeration degree enumeration rad enumeration mrad enumeration sr enumeration msr enumeration srad enumeration msrad enumeration C enumeration K enumeration atm enumeration bar enumeration mbar enumeration Torr enumeration mTorr enumeration mmHg enumeration Pa enumeration other enumeration arbitrary enumeration none |

simpleType yieldunitsType

| type | restriction of unitsType |
| --- | --- |
| used by | attribute yieldType/@units |
| facets | Kind Value annotation enumeration counts enumeration counts/(uCmg/cm2) enumeration counts/(uC1e15at/cm2) enumeration counts/(uCug/cm2) enumeration other enumeration arbitrary enumeration none |

XML Schema documentation generated by XMLSpy Schema Editor http://www.altova.com/xmlspy

# Endnotes

[]	E. Rauhala, N. P. Barradas, S. Fazinic, M. Mayer, E. Szilágyi, M. Thompson, Nucl. Instrum. Methods B244 (2006) 436

[]	N.P. Barradas, K. Arstila, G. Battistig, M. Bianconi, N. Dytlewski, C. Jeynes, E. Kótai, G. Lulli, M. Mayer, E. Rauhala, E. Szilágyi, M. Thompson, Nucl. Instrum. Methods B262 (2007) 282

[]	Consultants Meeting on Evaluation and Intercomparison of Software for Accelerator Science, 15-16 December 2003, Vienna, Austria

[]	http://www.w3.org/XML. XML is a World Wide Web Consortium (W3C) recommendation.

[]	http://www.spirit-ion.eu. SPIRIT represents an Integrated Infrastructure Initiative (I3) funded by the European Commission. The SPIRIT consortium integrates 11 leading ion beam facilities and 4 R&D providers from 6 member states and 2 associated states.

[]	http://www.nexusformat.org/Main_Page

# Text boxes























